Taste

---
Summary
- SpinalHDL introduction
- Differences with VHDL/Verilog
- Hardware description examples
  - By using abstractions
  - By using software engineering

---
Context :
- VHDL-2002 and Verilog-2005 are bottlenecks by many aspects
- VHDL-2008 and SV will not all save us (EDA support, features ...)

---
SpinalHDL introduction
- Open source, started in december 2014
- Focus on RTL description
- Thinked to be interoperable with existing tools
  - It generates simples VHDL/Verilog files (as an output netlist)
  - It can integrate VHDL/Verilog IP as blackbox
Abstraction level :
  - An RTL approach as VHDL/Verilog
  - If you want to, you can use many abstraction utils and also define new ones

---
By using an dedicated syntax (SpinalHDL)
val mySignal = Bool
val myRegister = Reg(UInt(4 bits))
val myRegisterWithReset = Reg(UInt(4 bits)) init(0)
mySignal := False
when(cond) {
   mySignal := True
   myRegister := myRegister + 1
   myRegisterWithReset := myRegisterWithReset + 1
}
[Speaker Notes: In VHDL you need to split the logic between combinatoral / sequancial with reset / sequancial without reset]

---
A timer implementation
class Timer(width : Int) extends Component{
   val io = new Bundle{
       val tick = in Bool
       val clear = in Bool
       val limit = in UInt(width bits)
       val full = out Bool
   }
   val counter = Reg(UInt(width bits))
   when(io.tick && !io.full){
       counter := counter + 1
   }
   when(io.clear){
       counter := 0
   }
   io.full := counter === io.limit
}

---
Having a Hand-shake bus of color and wanting to queue it ?
[Speaker Notes: In VHDL you need to split the logic between combinatoral / sequancial with reset / sequancial without reset]

---
In standard VHDL-2002
    fifo_inst : entity work.Fifo
        generic map (
        depth => 16,
        payload_width => 16
        )
        port map (
        clk => clk,
        reset => reset,
        push_valid => source_valid,
        push_ready => source_ready,
        push_payload(4 downto 0) => source_payload_r,
        push_payload(10 downto 5) => source_payload_g,
        push_payload(15 downto 11) => source_payload_b,
        pop_valid => sink_valid,
        pop_ready => sink_ready,
        pop_payload(4 downto 0) => sink_payload_r,
        pop_payload(10 downto 5) => sink_payload_g,
        pop_payload(15 downto 11) => sink_payload_b
        );
    signal source_valid : std_logic;
    signal source_ready : std_logic;
    signal source_r : unsigned(4 downto 0);
    signal source_g : unsigned(5 downto 0);
    signal source_b : unsigned(4 downto 0);
    signal sink_valid : std_logic;
    signal sink_ready : std_logic;
    signal sink_r : unsigned(4 downto 0);
    signal sink_g : unsigned(5 downto 0);
    signal sink_b : unsigned(4 downto 0);
[Speaker Notes: In VHDL you need to split the logic between combinatoral / sequancial with reset / sequancial without reset]

---
In SpinalHDL
val source, sink = Stream(RGB(5,6,5))
val fifo = StreamFifo(
   dataType = RGB(5,6,5),
   depth = 16
)
fifo.io.push << source
fifo.io.pop >> sink
[Speaker Notes: In VHDL you need to split the logic between combinatoral / sequancial with reset / sequancial without reset]

---
About Stream
case class Stream[T <: Data](payloadType : HardType[T]) extends Bundle {
   val valid = Bool
   val ready = Bool
   val payload = payloadType()
   def >>(sink: Stream[T]): Unit ={
       sink.valid := this.valid
       this.ready := sink.ready
       sink.payload := this.payload
   }
    def queue(size: Int): Stream[T] = {
       val fifo = new StreamFifo(payloadType, size)
       this >> fifo.io.push
       return fifo.io.pop
   }
}
Stream(RGB(5,6,5))
[Speaker Notes: In VHDL you need to split the logic between combinatoral / sequancial with reset / sequancial without reset]

---
Queuing in SpinalHDL
val source, sink = Stream(RGB(5,6,5))
val fifo = StreamFifo(
   dataType = RGB(5,6,5),
   depth = 16
)
fifo.io.push << source
fifo.io.pop >> sink
val source, sink = Stream(RGB(5,6,5))
source.queue(16) >> sink
SpinalHDL => 2 lines
VHDL => 29 lines
[Speaker Notes: In VHDL you need to split the logic between combinatoral / sequancial with reset / sequancial without reset]

---
Abstract arbitration
val source = Stream(RGB(5,6,5))
val sink = source.throwWhen(source.payload.isBlack).stage()
[Speaker Notes: In VHDL you need to split the logic between combinatoral / sequancial with reset / sequancial without reset]

---
Functional programming
val addresses = Vec(UInt(8 bits),4)
val key = UInt(8 bits)
val hits = addresses.map(address => address === key)
val hit = hits.reduce((a,b) => a || b)

---
Design introspection
val a = UInt(8 bits)
val b = UInt(8 bits)
val aCalcResult = complicatedLogic(a)
val aLatency = LatencyAnalysis(a,aCalcResult)
val bDelayed = Delay(b,cycleCount = aLatency)
val result = aCalcResult + bDelayed
[Speaker Notes: Because spinal build a netlist in the memory, you can use it to extract some information, for example latency (in cycle) between some points of you design. To do that, call LatencyAnalysis and give to it as argument some the start point, some check point and the end point of you path. It look for the shortest path and return how many cycle there is.]

---
FSM
val fsm = new StateMachine{
   val stateA = new State with EntryPoint
   val stateB = new State
   val stateC = new State
   val counter = Reg(UInt(8 bits)) init (0)
   io.result := False
   stateA.whenIsActive (goto(stateB))
   stateB
       .onEntry(counter := 0)
       .whenIsActive {
        counter := counter + 1
        when(counter === 4){
        goto(stateC)
        }
       }
       .onExit(io.result := True)
   stateC.whenIsActive (goto(stateA))
}

---
Abstract bus mapping
//Create a new AxiLite4 bus
val bus = AxiLite4(addressWidth = 12, dataWidth = 32)
//Create the factory which is able to create some bridging logic between the bus and some hardware
val factory = new AxiLite4SlaveFactory(bus)
//Create 'a' and 'b' as write only register
val a = factory.createWriteOnly(UInt(32 bits), address = 0)
val b = factory.createWriteOnly(UInt(32 bits), address = 4)
//Do some calculation
val result = a * b
//Make 'result' readable by the bus
factory.read(result(31 downto 0), address = 8)

---
SlaveFactory
AxiLite4SlaveFactory is only a part of something bigger and more abstract.

---
Briey SoC

---
Peripheral side
val apbBridge = Axi4ToApb3Bridge(
   addressWidth = 20,
   dataWidth = 32,
   idWidth = 4
)
val apbDecoder = Apb3Decoder(
   master = apbBridge.io.apb,
   slaves = List(
       gpioACtrl.io.apb	-> (0x00000, 4 kB),
       gpioBCtrl.io.apb -> (0x01000, 4 kB),
       uartCtrl.io.apb	-> (0x10000, 4 kB),
       timerCtrl.io.apb	-> (0x20000, 4 kB),
       vgaCtrl.io.apb -> (0x30000, 4 kB),
       core.io.debugBus	-> (0xF0000, 4 kB)
   )
)

---
CPU pipelined over 5 stages

---
Modular CPU framework
val plugins = List(
   new PcManagerSimplePlugin(resetVector = 0x00000000l),
   new IBusSimplePlugin(catchAccessFault = false),
   new DBusSimplePlugin(catchAccessFault = false),
   new DecoderSimplePlugin(catchIllegalInstruction = false),
   new RegFilePlugin,
   new IntAluPlugin,
   new FullBarrielShifterPlugin,
   new HazardSimplePlugin(
       bypassExecute = false,
       bypassMemory = false,
       bypassWriteBack = false
    ),
   new MulPlugin,
   new DivPlugin,
   new MachineCsr(...),
   new BranchPlugin(
       catchAddressMisaligned = false,
       prediction = DYNAMIC
    )
)
val cpu = new Cpu5Stage(plugins)

---
CPU framework - Connections
//Global definition of the Programm Counter concept
object PC extends Stageable(UInt(32 bits))
//Somewere in the PcManager plugin
fetch.insert(PC) := X
//Somewere in the MachineCsr plugin
Y := writeBack.input(PC)

---
CPU framework - Connections
//Somewhere in the Branch plugin
val jumpInterface = pcPlugin.createJumpInterface(stage = execute)
//Later in the branch plugin
jumpInterface.valid := ???
jumpInterface.payload := execute.input(PC) + execute.input(INSTRUCTION)(31 downto 20)

---
Some links SpinalHDL project
Compiler sources :
    - https://github.com/SpinalHDL/SpinalHDL
Online documentation :
    - https://spinalhdl.github.io/SpinalDoc/
Ready to use base project :
    - https://github.com/SpinalHDL/SpinalBaseProject
Communication channels :
    - spinalhdl@gmail.com
    - https://gitter.im/SpinalHDL/SpinalHDL
    - https://github.com/SpinalHDL/SpinalHDL/issues