Writing software to elaborate hardware (SpinalHDL)

---
Background / whoami
- Dolu1990 on github
- Active on open/free project
  - SpinalHDL (2015) / VexRiscv (2017) / NaxRiscv(2021) / VexiiRiscv (2023)
- Software / Hardware background
  - Industrial system / Electronic degree

---
Let’s use a software language
object Main extends App{
 println("Hello world")
}

---
Let’s use an hardware description library (HDL)

---
Let’s use an hardware description library (HDL)
import spinal.core._
object Main extends App{
 SpinalVerilog(new Timer)
}
class Timer extends Component {
 val increment = in(Bool())
 val counter = Reg(UInt(8 bits)) init(0)
 val full = out(counter === 255)
 when(increment){
   counter := counter + 1
 }
}

---
Let’s use an hardware description library (HDL)
module Timer (
 input wire increment,
 output wire full,
 input wire clk,
 input wire reset
);
 reg [7:0] counter;
 assign full = (counter == 8'hff);
 always @(posedge clk or posedge reset) begin
   if(reset) begin
     counter <= 8'h00;
   end else begin
     if(increment) begin
       counter <= (counter + 8'h01);
     end
   end
 end
endmodule
import spinal.core._
object Main extends App{
 SpinalVerilog(new Timer)
}
class Timer extends Component {
 val increment = in(Bool())
 val counter = Reg(UInt(8 bits)) init(0)
 val full = out(counter === 255)
 when(increment){
   counter := counter + 1
 }
}

---
Data structure / parameters
case class Pixel(width: Int) extends Bundle{
 val r, g, b = UInt(width bits)
}
case class Stream[T <: Data](dataType: HardType[T]) extends Bundle {
 val valid = Bool()
 val ready = Bool()
 val data = dataType()
}
val bus = Stream(Pixel(8))
bus.valid := False
bus.data.r := 0x11
bus.data.g := 0x22
bus.data.b := 0x33

---
Integrated linting
- Latches
- Combinatorial loops
- Unspecified clock crossing
- Undriven signals
- Width mismatch
- ...
LATCH DETECTED from the combinatorial signal (toplevel/result : out UInt[8 bits]), defined at ...
val cond = in Bool()
val result = out UInt(8 bits)
when(cond){
 result := 0
}

---
Integrated linting
val a,b,c = Bool()
c := b; b := a; a := c
COMBINATORIAL LOOP :
    (toplevel/a : Bool)
    (toplevel/b : Bool)
    (toplevel/c : Bool)
    (toplevel/a : Bool)
- Latches
- Combinatorial loops
- Unspecified clock crossing
- Undriven signals
- Width mismatch
- ...
LATCH DETECTED from the combinatorial signal (toplevel/result : out UInt[8 bits]), defined at ...
val cond = in Bool()
val result = out UInt(8 bits)
when(cond){
 result := 0
}

---
Integrated linting
val a,b,c = Bool()
c := b; b := a; a := c
COMBINATORIAL LOOP :
    (toplevel/a : Bool)
    (toplevel/b : Bool)
    (toplevel/c : Bool)
    (toplevel/a : Bool)
- Latches
- Combinatorial loops
- Unspecified clock crossing
- Undriven signals
- Width mismatch
- ...
class Toplevel(cdA : ClockDomain, cdB : ClockDomain) extends Component {
 val regA = cdA(Reg(Bool()))
 val regB = cdB(Reg(Bool()))
 regB := regA
}
CLOCK CROSSING VIOLATION :
- Source : (toplevel/regA : Bool) spinal.tester.code.Toplevel….(PresentationDsl.scala:1494)
- Source clock : (cdA_clk : Bool)
- Destination : (toplevel/regB : Bool) spinal.tester.code.Toplevel….(PresentationDsl.scala:1495)
- Destination clock : (cdB_clk : Bool)
LATCH DETECTED from the combinatorial signal (toplevel/result : out UInt[8 bits]), defined at ...
val cond = in Bool()
val result = out UInt(8 bits)
when(cond){
 result := 0
}

---
Using software to elaborate your hardware
if(featureEnabled){
 Reg(UInt(8 bits))
}
- Control flow : if / for
- Data collections : dynamic array / hash map / hash set
- Lambda function : reduce / fold / map / filter / ...
- OOP : class / software interface
- See https://spinalhdl.github.io/NaxRiscv-Rtd/main/NaxRiscv/abstraction/index.html

---
Using software to elaborate your hardware
for(i <- 0 to 2){
 Reg(UInt(8 bits))
}
- Control flow : if / for
- Data collections : dynamic array / hash map / hash set
- Lambda function : reduce / fold / map / filter / ...
- OOP : class / software interface
- See https://spinalhdl.github.io/NaxRiscv-Rtd/main/NaxRiscv/abstraction/index.html

---
Using software to elaborate your hardware
- Control flow : if / for
- Data collections : dynamic array / hash map / hash set
- Lambda function : reduce / fold / map / filter / ...
- OOP : class / software interface

---
Pipeline API

---
Pipeline API
val pip = new Pipeline()

---
Pipeline API
val pip = new Pipeline()
val PC = NamedType(UInt(32 bits))
pip(PC, 0) := 0x42

---
Pipeline API
val pip = new Pipeline()
val PC = NamedType(UInt(32 bits))
pip(PC, 0) := 0x42
val CALC = NamedType(UInt(32 bits))
pip(CALC, 2) := pip(PC, 2) + 0x11

---
Pipeline API
val pip = new Pipeline()
val PC = NamedType(UInt(32 bits))
pip(PC, 0) := 0x42
val CALC = NamedType(UInt(32 bits))
pip(CALC, 2) := pip(PC, 2) + 0x11
val x = pip(PC, 3) + 1
val y = pip(CALC, 4) + 0x22

---
Pipeline API
val pip = new Pipeline()
val PC = NamedType(UInt(32 bits))
pip(PC, 0) := 0x42
val CALC = NamedType(UInt(32 bits))
pip(CALC, 2) := pip(PC, 2) + 0x11
val x = pip(PC, 3) + 1
val y = pip(CALC, 4) + 0x22
pip.build()

---
Pipeline API
  wire [31:0] PC_0;
  wire [31:0] PC_3;
  wire [31:0] x;
  wire [31:0] CALC_2;
  wire [31:0] PC_2;
  wire [31:0] CALC_4;
  wire [31:0] y;
  wire [31:0] PC_1;
  reg [31:0] PC_0_regNext;
  reg [31:0] PC_1_regNext;
  reg [31:0] PC_2_regNext;
  wire [31:0] CALC_3;
  reg [31:0] CALC_2_regNext;
  reg [31:0] CALC_3_regNext;
  assign PC_0 = 32'h00000042;
  assign x = (PC_3 + 32'h00000001);
  assign CALC_2 = (PC_2 + 32'h00000011);
  assign y = (CALC_4 + 32'h00000022);
  assign PC_1 = PC_0_regNext;
  assign PC_2 = PC_1_regNext;
  assign PC_3 = PC_2_regNext;
  assign CALC_3 = CALC_2_regNext;
  assign CALC_4 = CALC_3_regNext;
  always @(posedge clk) begin
    PC_0_regNext <= PC_0;
    PC_1_regNext <= PC_1;
    PC_2_regNext <= PC_2;
    CALC_2_regNext <= CALC_2;
    CALC_3_regNext <= CALC_3;
  end
val pip = new Pipeline()
val PC = NamedType(UInt(32 bits))
pip(PC, 0) := 0x42
val CALC = NamedType(UInt(32 bits))
pip(CALC, 2) := pip(PC, 2) + 0x11
val x = pip(PC, 3) + 1
val y = pip(CALC, 4) + 0x22
pip.build()

---
Pipeline API
class Pipeline{
 //Define the pipeline data model
 val specs = LinkedHashMap[NamedType[Data], LinkedHashMap[Int, Data]]()
 //Define how we can access the pipeline
 def apply[T <: Data](what: NamedType[T], stageId: Int) = {
   val spec = specs.getOrElseUpdate(what.asInstanceOf[NamedType[Data]], new LinkedHashMap[Int, Data])
   spec.getOrElseUpdate(stageId, what().setName(what.getName + "_" + stageId)).asInstanceOf[T]
 }
 //Translate specs into hardware
 def build(): Unit = {
   for ((what, nodes) <- specs) {
     for (i <- nodes.keys.min until nodes.keys.max) {
       apply(what, i + 1) := RegNext(apply(what, i))
     }
   }
 }
}

---
Pipeline API
class Pipeline{
 //Define the pipeline data model
 val specs = LinkedHashMap[NamedType[Data], LinkedHashMap[Int, Data]]()
 //Define how we can access the pipeline
 def apply[T <: Data](what: NamedType[T], stageId: Int) = {
   val spec = specs.getOrElseUpdate(what.asInstanceOf[NamedType[Data]], new LinkedHashMap[Int, Data])
   spec.getOrElseUpdate(stageId, what().setName(what.getName + "_" + stageId)).asInstanceOf[T]
 }
 //Translate specs into hardware
 def build(): Unit = {
   for ((what, nodes) <- specs) {
     for (i <- nodes.keys.min until nodes.keys.max) {
       apply(what, i + 1) := RegNext(apply(what, i))
     }
   }
 }
}

---
Pipeline API
class Pipeline{
 //Define the pipeline data model
 val specs = LinkedHashMap[NamedType[Data], LinkedHashMap[Int, Data]]()
 //Define how we can access the pipeline
 def apply[T <: Data](what: NamedType[T], stageId: Int) = {
   val spec = specs.getOrElseUpdate(what.asInstanceOf[NamedType[Data]], new LinkedHashMap[Int, Data])
   spec.getOrElseUpdate(stageId, what().setName(what.getName + "_" + stageId)).asInstanceOf[T]
 }
 //Translate specs into hardware
 def build(): Unit = {
   for ((what, nodes) <- specs) {
     for (i <- nodes.keys.min until nodes.keys.max) {
       apply(what, i + 1) := RegNext(apply(what, i))
     }
   }
 }
}

---
Pipeline API
class Pipeline{
 //Define the pipeline data model
 val specs = LinkedHashMap[NamedType[Data], LinkedHashMap[Int, Data]]()
 //Define how we can access the pipeline
 def apply[T <: Data](what: NamedType[T], stageId: Int) = {
   val spec = specs.getOrElseUpdate(what.asInstanceOf[NamedType[Data]], new LinkedHashMap[Int, Data])
   spec.getOrElseUpdate(stageId, what().setName(what.getName + "_" + stageId)).asInstanceOf[T]
 }
 //Translate specs into hardware
 def build(): Unit = {
   for ((what, nodes) <- specs) {
     for (i <- nodes.keys.min until nodes.keys.max) {
       apply(what, i + 1) := RegNext(apply(what, i))
     }
   }
 }
}

---
Pipeline API
  wire [31:0] PC_0;
  wire [31:0] PC_3;
  wire [31:0] x;
  wire [31:0] CALC_2;
  wire [31:0] PC_2;
  wire [31:0] CALC_4;
  wire [31:0] y;
  wire [31:0] PC_1;
  reg [31:0] PC_0_regNext;
  reg [31:0] PC_1_regNext;
  reg [31:0] PC_2_regNext;
  wire [31:0] CALC_3;
  reg [31:0] CALC_2_regNext;
  reg [31:0] CALC_3_regNext;
  assign PC_0 = 32'h00000042;
  assign x = (PC_3 + 32'h00000001);
  assign CALC_2 = (PC_2 + 32'h00000011);
  assign y = (CALC_4 + 32'h00000022);
  assign PC_1 = PC_0_regNext;
  assign PC_2 = PC_1_regNext;
  assign PC_3 = PC_2_regNext;
  assign CALC_3 = CALC_2_regNext;
  assign CALC_4 = CALC_3_regNext;
  always @(posedge clk) begin
    PC_0_regNext <= PC_0;
    PC_1_regNext <= PC_1;
    PC_2_regNext <= PC_2;
    CALC_2_regNext <= CALC_2;
    CALC_3_regNext <= CALC_3;
  end
val pip = new Pipeline()
val PC = NamedType(UInt(32 bits))
pip(PC, 0) := 0x42
val CALC = NamedType(UInt(32 bits))
pip(CALC, 2) := pip(PC, 2) + 0x11
val x = pip(PC, 3) + 1
val y = pip(CALC, 4) + 0x22
pip.build()

---
VexiiRiscv
- RISC-V softcore
- Very large design space
- Can run linux (RV32 / RV64 IMACSU)
- Multiple issue
- Early + late ALU
- 5.24 coremark/Mhz 2.50 dhystone/Mhz
- https://github.com/SpinalHDL/VexiiRiscv

---
VexiiRiscv : Pipeline API

---
VexiiRiscv : Pipeline API
val alu = new pipeline.Execute(0) {
 val TAKEN = insert(RS1 === RS2);
}

---
VexiiRiscv : Pipeline API
val alu = new pipeline.Execute(0) {
 val TAKEN = insert(RS1 === RS2);
}
val branch = new pipeline.Execute(1) {
 flushPort.valid := alu.TAKEN
 pcPort.valid := alu.TAKEN
 pcPort.pc := ..
}

---
VexiiRiscv : Pipeline API
val aluAt = 0
val branchAt = 1
...
val alu = new pipeline.Execute(aluAt) {
 val TAKEN = insert(RS1 === RS2);
}
val branch = new pipeline.Execute(branchAt) {
 flushPort.valid := alu.TAKEN
 pcPort.valid := alu.TAKEN
 pcPort.pc := ..
}

---
VexiiRiscv : Decoding / Scheduling

---
VexiiRiscv : Specification structure
case class OpSpec(
 encoding : String,
 mayFlush : Boolean,
 sideEffect: Boolean,
)

---
VexiiRiscv : Define instructions spec
case class OpSpec(
 encoding : String,
 mayFlush : Boolean,
 sideEffect: Boolean,
)
val ADD = OpSpec("000-----0110011", false, false)
val CALL = OpSpec("--------1101111", true, false)
val SW = OpSpec("100-----1100011", false, true)

---
VexiiRiscv : Collect the specifications
case class OpSpec(
 encoding : String,
 mayFlush : Boolean,
 sideEffect: Boolean,
)
val ADD = OpSpec("000-----0110011", false, false)
val CALL = OpSpec("--------1101111", true, false)
val SW = OpSpec("100-----1100011", false, true)
val opsSpec = List(ADD, CALL, SW)

---
VexiiRiscv : Decode
case class OpSpec(
 encoding : String,
 mayFlush : Boolean,
 sideEffect: Boolean,
)
val ADD = OpSpec("000-----0110011", false, false)
val CALL = OpSpec("--------1101111", true, false)
val SW = OpSpec("100-----1100011", false, true)
val opsSpec = List(ADD, CALL, SW)
val instruction = in Bits(32 bits)
val withSideEffects = Symplify(
 input = instruction,
 trueTerms = opsSpec.filter(_.sideEffect).map(_.encoding),
 falseTerms = opsSpec.filter(!_.sideEffect).map(_.encoding)
)

---
No more toplevel / design space
class VexiiRiscv(...) extends Component{
 val database = ...
 val host = ...
}
val plugins = ArrayBuffer[Hostable]()
plugins += new fetch.FetchPipelinePlugin()
plugins += new fetch.PcPlugin(resetVector)
plugins += new fetch.FetchL1Plugin(...)
plugins += new prediction.BtbPlugin(...)
plugins += new prediction.GSharePlugin (...)
plugins += new prediction.HistoryPlugin(...)
...
plugins += new execute.SimdAddPlugin(...)
val cpu = VexiiRiscv(plugins)

---
Custom instruction
  object SimdAddPlugin {
   val ADD4 = IntRegFile.TypeR(M"0000000----------000-----0001011")
 }
 class SimdAddPlugin(val layer: LaneLayer) extends ExecutionUnitElementSimple(layer) {
   val logic = during setup new Logic {
     awaitBuild()
     val wb = newWriteback(ifp, 0)
     val add4 = add(SimdAddPlugin.ADD4).spec
     add4.addRsSpec(RS1, executeAt = 0)
     add4.addRsSpec(RS2, executeAt = 0)
     uopRetainer.release()
     val process = new el.Execute(id = 0) {
       val rs1 = el(IntRegFile, RS1).asUInt
       val rs2 = el(IntRegFile, RS2).asUInt
       val rd = UInt(32 bits)
       rd( 7 downto 0) := rs1( 7 downto 0) + rs2( 7 downto 0)
       rd(16 downto 8) := rs1(16 downto 8) + rs2(16 downto 8)
       rd(23 downto 16) := rs1(23 downto 16) + rs2(23 downto 16)
       rd(31 downto 24) := rs1(31 downto 24) + rs2(31 downto 24)
       wb.valid := SEL
       wb.payload := rd.asBits
     }
   }
 }
}

---
How to lower barriers to hardware design ?
- VHDL / [System]Verilog alternatives
  - SpinalHDL, Chisel, Migen, Amaranth, ...
- Hardware design can leverage software engineering
  - API / Tooling / abstraction
  - New pool of people profiles
- Closed industry tools limits the scale of free/open-source hardware
  - Alternatives (Verilator, GHDL, IVerilog, openroad, ..)

---
Question ?