Coroutines applied to a tilelink interconnect elaboration

---
Fibers applied to a tilelink interconnect elaboration

---
wire axi_awvalid;
wire axi_awready;
wire [19:0] axi_awaddr;
wire [3:0] axi_awid;
wire [7:0] axi_awlen;
wire [2:0] axi_awsize;
wire axi_wvalid;
wire axi_wready;
wire [31:0] axi_wdata;
wire [3:0] axi_wstrb;
wire axi_wlast;
wire axi_bvalid;
wire axi_bready;
wire [3:0] axi_bid;
wire [1:0] axi_bresp;
wire axi_arvalid;
wire axi_arready;
wire [19:0] axi_araddr;
wire [3:0] axi_arid;
wire [7:0] axi_arlen;
wire [2:0] axi_arsize;
wire axi_rvalid;
wire axi_rready;
wire [31:0] axi_rdata;
wire [3:0] axi_rid;
wire [1:0] axi_rresp;
wire axi_rlast;
Wire sea
wire [19:0] apb_PADDR;
wire [0:0] apb_PSEL;
wire apb_PENABLE;
wire apb_PREADY;
wire apb_PWRITE;
wire [31:0] apb_PWDATA;
wire [31:0] apb_PRDATA;

---
Bus definition
case class Apb3(addressWidth: Int,
        dataWidth : Int) extends Bundle with IMasterSlave {
 val PADDR = UInt(addressWidth bits)
 val PSEL = Bool()
 val PENABLE = Bool()
 val PREADY = Bool()
 val PWRITE = Bool()
 val PWDATA = Bits(dataWidth bits)
 val PRDATA = Bits(dataWidth bits)
 override def asMaster(): Unit = {
   out(PADDR, PSEL, PENABLE, PWRITE, PWDATA)
   in(PREADY, PRDATA)
 }
}
val myBus = Apb3(20, 32)
val myBus = Apb3(
 addressWidth = 20,
 dataWidth = 32
)

---
Software API
val commonBus = Apb3(
 addressWidth = 20,
 dataWidth = 32
)
val apbDecoder = Apb3Decoder(
 master = commonBus,
 slaves = List(
   gpioBus -> (0x2000, 4 kB),
   uartBus -> (0x5000, 4 kB)
 )
)
val uartBus = Apb3(
 addressWidth = 12,
 dataWidth = 32
)
val gpioBus = Apb3(
 addressWidth = 12,
 dataWidth = 32
)

---
Automation
val cpu0Bus, cpu1Bus = Axi4(32, 32, idWidth = 2)
val mainBus = Axi4(32, 32, idWidth = 4)
val ramBus = Axi4(16, 32, idWidth = 6)
val peripheralBus = Axi4(20, 32, idWidth = 6)
val gpioBus, uartBus = Axi4(12, 32, idWidth = 8)
val axiCrossbar = Axi4CrossbarFactory()
axiCrossbar.addSlaves(
 mainBus -> (0x00000000, 4 GB),
 ramBus -> (0x80000000, 64 kB),
 peripheralBus -> (0x10000000, 1 MB),
 gpioBus -> ( 0x2000, 4 kB),
 uartBus -> ( 0x5000, 4 kB)
)
axiCrossbar.addConnections(
 cpu0Bus -> List(mainBus),
 cpu1Bus -> List(mainBus),
 mainBus -> List(ramBus, peripheralBus),
 peripheralBus -> List(gpioBus, uartBus)
)
axiCrossbar.build()

---
Decentralization
import spinal.lib.bus.tilelink.fabric.Node
val cpu0Bus, cpu1Bus = Node()
val mainBus = Node()
val ramBus = Node()
val peripheralBus = Node()
val gpioBus, uartBus = Node()
mainBus << List(cpu0Bus, cpu1Bus)
ramBus at 0x80000000 of mainBus
peripheralBus at 0x10000000 of ramBus
gpioBus at 0x2000 of peripheralBus
uartBus at 0x5000 of peripheralBus
val bus = tilelink.fabric.Node()

---
Decentralization
class Connection(val m : Node, val s : Node){
 val thread = Fiber build new Area{
   // Connect the m.decoder to the s.arbiter
 }
class Node extends Area{
 // Node data model
 val bus = Handle[tilelink.Bus]()
 val ups = ArrayBuffer[Connection]()
 val downs = ArrayBuffer[Connection]()
 //Fork an elaboration thread
 val thread = Fiber build new Area{
   // Generate the required arbiter / decoder logic.
 }

---
Future, Promise, Async, Fibers...
val bus = Handle[tilelink.Bus]
val thread1 = Fiber build new Area{
 println("Thread 1 start")
 //Will wait on bus.load (from thread 2)
 bus.a.valid := False
 bus.a.address := 42
 println("Thread 1 done")
val thread2 = Fiber build new Area{
 println("Thread 2 start")
 val config = tilelink.BusParameter.simple(
   addressWidth = 32,
   dataWidth = 64,
   sizeBytes = 16,
   sourceWidth = 4
 )
 //Will allow thread 1 to continue
 bus load tilelink.Bus(config)
 println("Thread 2 done")
Thread 1 start
Thread 2 start
Thread 2 done
Thread 1 done
assign bus_a_valid = 1'b0;
assign bus_a_address = 32'h00000042;

---
Negotiation
class Node extends Area{
 // Node data model
 val proposed = Handle[M2sSupport]()
 val supported = Handle[M2sSupport]()
 val parameters = Handle[M2sParameters]()
  val bus = Handle[Bus]()
 //Fork an elaboration thread
 val thread = Fiber build new Area{
    // Do the Negotiation
   // Generate the required arbiter / decoder logic.
 }

---
Master example
case class Cpu() extends Area {
 val node = Node.master()
 val thread = Fiber build new Area {
    // Negotiate things
   node.proposed load M2sSupport(
     addressWidth = 32,
     dataWidth = 64,
     transfers = M2sTransfers(
       get = SizeRange.upTo(64),
       putFull = SizeRange.upTo(64)
     )
   )
   node.parameters load M2sParameters(
     support = node.supported,
     sourceCount = 4
   )
   // Implement the actual CPU hardware
   node.bus.a.valid := False
   node.bus.a.address := 0x42
 }

---
Adapter example
class WidthAdapter() extends Area{
 val up = Node.slave()
 val down = Node.master()
 val thread = Fiber build new Area{
   down.proposed load up.proposed
   up.supported load down.supported.copy(
      dataWidth = up.proposed.dataWidth
    )
   down.parameters load up.parameters.copy(
      dataWidth = down.supported.dataWidth
    )
   val bridge = new WidthAdapter(up.bus.p, down.bus.p)
   bridge.io.up << up.bus
   bridge.io.down >> down.bus
 }

---
Deployment
val cpu = Cpu()
val adapter = WidthAdapter()
val peripheral = Peripheral()
adapter.up << cpu.node
peripheral.node at 0x2000 of adapter.down

---
Introspection
class CustomTag(val str : String) extends SpinalTag
val counter = Reg(UInt(8 bits))
counter := counter + 1
counter.addTag(new CustomTag("hello"))
counter.addTag(new CustomTag("miaou"))
counter.foreachTag{
 case ct : CustomTag => println(ct.str)
 case _ =>
hello
miaou

---
Introspection
  trait MemoryConnection extends SpinalTag {
   def m : SpinalTagReady
   def s : SpinalTagReady
   def mapping : SizeMapping
   override def toString = s"$m $s $mapping"
 }
val tag = new MemoryConnection{
 def m = peripheralBus
 def s = gpioBus
 def mapping = SizeMapping(0x5000, 0x1000)
peripheralBus.addTag(tag)
gpioBus.addTag(tag)

---
Introspection
def visit(node : SpinalTagReady, level : Int){
 node.foreachTag{
   case mc : MemoryConnection if mc.m == node => {
     println(" " * level + mc)
     visit(mc.s, level + 1)
   }
   case _ =>
 }
visit(cpu0Bus, 0)
cpu0Bus mainBus 0 100000000
  mainBus ramBus 40000000 10000
  mainBus peripheralBus 10000000 100000
    peripheralBus gpioBus 2000 1000
    peripheralBus uartBus 5000 1000

---
Interoperability
class TilelinkToAxiBridge() extends Area{
 val up = tilelink.fabric.Node.slave()
 val down = axi4.fabric.Node.master()
 val tag = new MemoryConnection {
   def m = peripheralBus
   def s = apbBus
   def mapping = SizeMapping(0, ...)
 }
 up.add(tag)
 down.add(tag)
 val thread = Fiber build new Area{
   // Handle the negotiation from Tilelink to AXI
   // ...
   // Generate the hardware
   // ...
 }

---
Question ?
- Open Discussion about the tilelink interconnect API / framework :
  - https://github.com/SpinalHDL/SpinalHDL/discussions/1115
- Roadmap
  - Tilelink interconnect with
    - memory coherency
    - L2 cache
  - NaxRiscv with tilelink memory coherency
- Looking for buddies :)

---
Miaou
Wuff