NaxRiscv
An open-source OoO superscalar softcore

---
Background / whoami
- Charles Papon (Dolu1990)
- Few projects
  - SpinalHDL
  - VexRiscv
  - NaxRiscv
- Hardware / Software mix
- Do not have a computer science degree

---
NaxRiscv in short
- RV32/RV64 IMACSU (Linux ready)
- Out of order / superscalar
- Free / Open source (MIT)
- Target FPGA with distributed RAM
- Many paradigm experimentation with alternative HDL
- ~75 FPS Chocolate-doom (@100Mhz / linux)
https://twitter.com/i/status/1493996880593887235

---
Performances / Area
- RV32IMASU, 2 decode, 3 issue (2 ALU, 1 shared EU)
  - Dhrystone : 2.64 DMIPS/Mhz 1.48 IPC (-O3 -fno-common -fno-inline)
  - Coremark : 4.70 Coremark/Mhz 1.19 IPC
  - Embench-iot : 1.55 baseline 1.32 IPC
- On Artix 7 speed grade 3 :
  - 14.6 KLUT, 9.8 KFF, 12.5 BRAM, 4 DSP
  - 145 Mhz (360 Mhz on Kintex ultrascale+ grade 3)
- RV64IMASU, same FPGA/config
  - 19.5 KLUT, 12.0 KFF, 12.5 BRAM, 16 DSP
  - 140 Mhz

---
Architecture (as configured in the last slide)
- 2 decode, 3 issue
- 64 physical register, 64 entry ROB
- 4KB GShare, 4KB BTB (both 1 way), RAS
- I$ D$ each have 16 KB (4 ways)
- I$ D$ each have 192 TLB (2+4 ways)

---
Dispatch / Issue Queue
- Shared between execution units
- 32 entries, grouped by “wave”, (ex: 2x16)
- Older first, no compression
- Matrix design, removal on completion

---
LSU (load)
- Speculative wake (hit prediction)
- load to use latency :
  - 3 cycle (hit predicted OK)
  - 6 cycle (miss predicted)
  - Full flush (hit predicted KO)
- AGU to D$ bypass
- RF written 1 cycle before completion
- 16 entries

---
LSU (store)
- 4 pipelines
- Dependencies
  - Address through IQ
  - Data directly read RF
- 16 entries

---
Simulation
- Based on Verilator (~150-200 Khz on Ryzen 3900)
- Lock-step checks against Spike (life saver)
- Can emit Gem5-O3 / Konata traces

---
Exploring hardware description paradigms
- A few things first
  - Stopped writing VHDL/[System]Verilog in 2016
  - NaxRiscv => Scala + SpinalHDL
  - Paradigm : You write software which use an API that generate hardware
    - SpinalHDL / Chisel / Migen / Amaranth HDL / …
- 4 key concepts in NaxRiscv
  - Composable toplevel
  - Multithreaded elaboration
  - Pipelining framework
  - Software engineering
Be aware, there will be code in the next slides !

---
class NaxRiscv(plugins : Seq[Plugin]) extends Component{
   val database = new DataBase
   val framework = NaxScope(database) on new Framework(plugins)
}

---
val plugins = ArrayBuffer[Plugin]()
plugins ++= List(
   new PcPlugin(),
   new FetchCachePlugin(16 KB),
   new DecoderPlugin(),
   new DispatchPlugin(slotCount = 32),
   new CommitPlugin()
   ...
)
plugins ++= List(
   new ExecutionUnitBase("ALU0"),
   new IntFormatPlugin("ALU0"),
   new SrcPlugin("ALU0"),
   new IntAluPlugin("ALU0"),
   new ShiftPlugin("ALU0" ),
   new BranchPlugin("ALU0")
)
new NaxRiscv(plugins)
plugins ++= List(
   new ExecutionUnitBase("ALU1"),
   new IntFormatPlugin("ALU1"),
   new SrcPlugin("ALU1"),
   new IntAluPlugin("ALU1"),
   new ShiftPlugin("ALU1" ),
   new BranchPlugin("ALU1")
)
Wanna a second execution unit ?

---
Plugin / SIMD ADD8
class SimdAddPlugin(euId : String) extends Plugin {
   val ADD8 = IntRegFile.TypeR(M"0000000----------000-----0001011")
   val SEL = Stageable(Bool())
   val setup = create early new Area{
       // ...
   }
   val logic = create late new Area{
       // ...
   }
}

---
 val setup = create early new Area{
     val eu = findService[ExecutionUnitBase](_.euId == euId)
     eu.retain()
     eu.addMicroOp(ADD8)
     eu.setCompletion(ADD8, stageId = 0)
     eu.setStaticWake(ADD8, stageId = 0)
     eu.setDecodingDefault(SEL, False)
     eu.addDecoding(ADD8, SEL, True)
     val intFormat = findService[IntFormatPlugin](_.euId == euId)
     val writeback = intFormat.access(stageId = 0, writeLatency = 0)
 }

---
 val logic = create late new Area{
     val eu = setup.eu
     val writeback = setup.writeback
     val stage = eu.getExecute(stageId = 0)
     val rs1 = stage(eu(IntRegFile, RS1)).asUInt
     val rs2 = stage(eu(IntRegFile, RS2)).asUInt
     val rd = UInt(32 bits)
     rd( 7 downto 0) := rs1( 7 downto 0) + rs2( 7 downto 0)
     rd(16 downto 8) := rs1(16 downto 8) + rs2(16 downto 8)
     rd(23 downto 16) := rs1(23 downto 16) + rs2(23 downto 16)
     rd(31 downto 24) := rs1(31 downto 24) + rs2(31 downto 24)
     writeback.valid := stage(SEL)
     writeback.payload := rd.asBits
     eu.release()
 }
https://spinalhdl.github.io/NaxRiscv-Rtd/main/NaxRiscv/execution_units/index.html#custom-instruction

---
val plugins = ArrayBuffer[Plugin]()
...
plugins ++= List(
   new ExecutionUnitBase("ALU0"),
   new IntFormatPlugin("ALU0"),
   new SrcPlugin("ALU0"),
   new IntAluPlugin("ALU0"),
   new ShiftPlugin("ALU0" ),
   new BranchPlugin("ALU0")
)
plugins += new SimdAddPlugin("ALU0")
plugins += new SimdAddPlugin("ALU1")
new NaxRiscv(plugins)
plugins ++= List(
   new ExecutionUnitBase("ALU1"),
   new IntFormatPlugin("ALU1"),
   new SrcPlugin("ALU1"),
   new IntAluPlugin("ALU1"),
   new ShiftPlugin("ALU1" ),
   new BranchPlugin("ALU1")
)

---
Status / Future
- RV32/RV64 IMACSU configs seems stable so far
  - Linux / FreeRTOS / riscv-tests / riscv-arch-test OK
- JTAG / OpenOCD / GDB supported (RISCV External Debug Support 0.13.2)
- Planning :
  - FPU → Debian support
  - Multicore / Memory coherency
- GIT : https://github.com/SpinalHDL/NaxRiscv
- Integrated in Litex for FPGA deployments
  - python3 -m litex_boards.targets.digilent_nexys_video --cpu-type=naxriscv --with-video-framebuffer --with-spi-sdcard --with-ethernet --build --load

---
Miaou

---
Wuff

---
class SimdAddPlugin(val euId : String) extends ExecutionUnitElementSimple(euId, staticLatency = true) {
 override def euWritebackAt = 0
 override val setup = create early new Setup{
   add(SimdAddPlugin.ADD4)
 }
 override val logic = create late new Logic{
   val process = new ExecuteArea(stageId = 0) {
     val rs1 = stage(eu(IntRegFile, RS1)).asUInt
     val rs2 = stage(eu(IntRegFile, RS2)).asUInt
     val rd = UInt(32 bits)
     rd( 7 downto 0) := rs1( 7 downto 0) + rs2( 7 downto 0)
     rd(16 downto 8) := rs1(16 downto 8) + rs2(16 downto 8)
     rd(23 downto 16) := rs1(23 downto 16) + rs2(23 downto 16)
     rd(31 downto 24) := rs1(31 downto 24) + rs2(31 downto 24)
     wb.payload := rd.asBits
   }
 }
}

---
class CommitPlugin extends Plugin {
   val setup = create early new Area {
       val jump = getService[JumpService].newJumpPort(10)
   }
   val logic = create late new Area {
       setup.jump.valid := ???
       setup.jump.payload := ???
   }
}
trait JumpService extends Service{
   def newJumpPort(priority : Int) : Flow[UInt]
}
class PcPlugin extends Plugin with JumpService{
   override def newJumpPort(priority: Int) = {...}
   val logic = create late new Area {
       val pc = Reg(UInt(32 bits))
       ...
   }
}
Rawrrrr

---
Likely to be applicable to other alternative HDL

---
class PcPlugin extends Plugin {
   val logic = ...{
       val pcReg = Reg(UInt(32 bits))
       getService[FetchPlugin].pipeline.stages(0)(PC) := pcReg
   }
}
class FetchCachePlugin extends Plugin{
   val logic = ...{
       getService[FetchPlugin].pipeline.stages(2)(PC) === wayTag
   }
}
object PC extends Stageable(UInt(32 bits))

---
class FetchCachePlugin extends Plugin{
   val logic = ...{
       getService[FetchPlugin].pipeline.stages(2)(PC) === wayTag
   }
}
class FetchPlugin() extends Plugin {
   val pipeline = create early new Pipeline {
       val stages = Array.fill(3)(newStage())
 ...
   }
   val lock = Lock()
   val builder = create late new Area{
       lock.await()
       pipeline.build()
   }
}