 From the RISC-V spec to a low-tech SoC
passing by SpinalHDL, VexRiscv and OpenOCD
Dolu1990, FSiC, 2019

---
In short, I'm involved into :
- SpinalHDL (Alternative to VHDL/SystemVerilog for digital netlist description)
- VexRiscv (RISC-V CPU)

---
From RISC-V to VexRiscv (CPU implementation)
- RV32I[M][C]
- Implemented in SpinalHDL
  - Automated instruction decoding generation (Quine–McCluskey)
  - Automated pipelining (from 2 stages to 4 + X fetch stages)
  - CPU composability and customisation (The parametrization hold the behaviour)
  - Can't do that with VHDL/SystemVerilog on current synthesis tools
- Some resources about it :
  - https://github.com/SpinalHDL/VexRiscv#add-a-custom-instruction-to-the-cpu-via-the-plugin-system
  - https://tomverbeure.github.io/rtl/2018/12/06/The-VexRiscV-CPU-A-New-Way-To-Design.html

---
SpinalHDL, what it is, what it isn’t
- Not a even driven language
- Not a High Level Synthesis (HLS)
- Not a data flow language
- Not a language
- It is an hardware description library (SpinalHDL) implemented in a general purpose programming language (Scala)
- The hardware netlist is elaborated from the software runtime, not a compilation.

---
SpinalHDL API, not so far from a regular HDL
val myRegister = Reg(UInt(4 bits))
when(cond) {
   myRegister := myRegister + 1
}
val mySignal = Bool
mySignal := ! myRegister.msb

---
Software as an elaboration tool
  BLUE => Elaboration software
  RED => SpinalHDL API
  val a,b,c = UInt(8 bits)
  val list = List(a,b,c)
  for(element <- list){
      element := U(0)
  }

---
Software as an elaboration tool
- Object oriented programming
- Functional programming
- Inheritance
- Software collection (Dynamic lists, Map/Dictionary, Set)
- ...

---
Interconnect
- Nothing complicated here
  - 1 to N (decoder)
  - N to 1 (arbiter)

---
val interconnect = PipelinedMemoryBusInterconnect()
interconnect.addSlaves(
 ram.io.bus -> SizeMapping(0x00000, 64 kB),
 flash.io.bus -> SizeMapping(0x80000, 512 kB),
 peripherals.io.bus -> SizeMapping(0x70000, 64 kB)
)
interconnect.addMasters(
 cpu.io.iBus -> List(ram.io.bus, flash.io.bus),
 cpu.io.dBus -> List(ram.io.bus, flash.io.bus, peripherals.io.bus)
)
interconnect.build()

---
class PipelinedMemoryBusInterconnect{
   class SlaveInfo(bus : PipelinedMemoryBus, mapping : SizeMapping)
   class MasterInfo(bus : PipelinedMemoryBus, slaves : List[PipelinedMemoryBus])
   val slaves = ArrayBuffer[SlaveInfo]()
   val masters = ArrayBuffer[MasterInfo]()
   def addSlave(s : PipelinedMemoryBus, mapping : SizeMapping) = {
       slaves += new SlaveInfo(s, mapping)
   }
   def addMaster(m : PipelinedMemoryBus, slaves : List[PipelinedMemoryBus]) = {
       masters += new MasterInfo(m, slaves)
   }
   def build(): Unit ={ … }
}
class PipelinedMemoryBusInterconnect{
   val slaves = HashMap[PipelinedMemoryBus, SizeMapping]()
   val masters = HashMap[PipelinedMemoryBus, List[PipelinedMemoryBus]]()
   def addSlave(s : PipelinedMemoryBus, mapping : SizeMapping) = {
       slaves(s) = mapping
   }
   def addMaster(m : PipelinedMemoryBus, slaves : List[PipelinedMemoryBus]) = {
       masters(m) = slaves
   }
   def build() : Unit = {
for((master, slaves) <- masters){
        // Generate decoders
       }
       for((slave, mapping) <- masters){
        // Generate arbiters
       }
       // Connect decoders to arbiters
    }
}
  def build(): Unit ={
     for(m <- masters){
        // Generate decoders
     }
     for(s <- slaves){
        // Generate arbiters
     }
     // Connect decoders to arbiters
 }
SpinalHDL: Software generated hardware - ORConf 2018

---
CPU : Debug interface
- A CPU without a debug interface can be a nightmare
- Many opensource CPU do not implement one :(
- Minimal requirements
  - CPU controls (reset, run, halt, step)
  - CPU status (halted, breakpointed)
  - CPU god-mode (push instruction, read the result)
  - External interface (JTAG)

---
OpenOCD
- What it do :
  - Abstract the hardware to the debugger
  - Provide many JTAG drivers
- What is required to support a new CPU :
  - A set of C functions
OpenOCD
USB
FTDI
JTAG
SoC

---
OpenOCD : Adding a new target
struct target_type vexriscv_target = {
.name = "vexriscv",
.target_create = vexriscv_target_create,
.examine = vexriscv_examine,
.halt = vexriscv_halt,
.resume = vexriscv_resume,
.step = vexriscv_step,
.add_breakpoint = vexriscv_add_breakpoint,
.remove_breakpoint = vexriscv_remove_breakpoint,
.read_memory = vexriscv_read_memory,
.write_memory = vexriscv_write_memory,
 ...
};
Write 0x89abcdef @ 0x1234567
Push instruction :
lui 0x89abc, x1
ori x1, x1, 0xdef
lui 0x01234, x2
sw x1, x2(0x567)
OpenOCD
USB
FTDI
JTAG
SoC

---
SoC toplevel hell
- Imagine X did a SoC, then Y want to extend it for it’s own purposes, this usualy result in :
  - Y forking X SoC, and modify the toplevel (no way back, painefull pullrequest)
  - Y adding parametrization into X SoC to cover its use cases (messy SoC toplevel)
- Now Z want to extend the X SoC for it’s own purposes, ...
- Parametrization isn’t good enough !
- Solution attempt
  - Composing a SoC by having generators and dependencies

---
A stairway to the heaven (I believe)
class SocX {
   val soc = new SocBase()
   val gpioA = soc.addGpio(0xA000, 32)
}
class SocZ {
   val soc = new SocBase()
   val gpioA = soc.addGpio(0xA000, 32)
    val dma = system.addDma(0xB000, ...)
   val adc = system.addAdc(0xC000, ...)
   dma.addInputStream(adc.stream)
   val dac = system.addDac(0xC100, ...)
   dma.addOutputStream(dac.stream)
}
class SocBase extends Generator{
   val cpu = new Generator { ... }
   val interconnect = new Generator { ... }
   def addGpio(address : Int, width : Int) = new Generator {
       interconnect.dependencies += this
       add task new Area {
        val peripheral = Apb3Gpio(width)
        interconnect.map(peripheral.io.bus, address, 4 KiB)
        val gpio = master(TriStateArray(width))
        gpio <> ctrl.io.gpio
       }
   }
}
class SocY {
   val soc = new SocBase()
   val gpioA = soc.addGpio(0xA000, 12)
   val gpioB = soc.addGpio(0xA100, 16)
   val gpioC = soc.addGpio(0xA200, 20)
}
class SocBase extends Generator{
   val cpu = new Generator { ... }
   val interconnect = new Generator { ... }
   def addGpio(address : Int, width : Int) = new Generator {
        interconnect.dependencies += this
add task new Area { //Hardware generation here }
    }
}

---
Multipass elaboration
class SocBase extends Generator{
   val cpu = new Generator { ... }
   val interconnect = new Generator { ... }
   def addGpio(address : Int, width : Int) = new Generator {
        interconnect.dependencies += this
add task new Area { //Hardware generation here }
    }
   def addAdc(address : Int) = new Generator { … }
   def addDac(address : Int) = new Generator { … }
   def addDma(address : Int) = new Generator { … }
}
class SocBase extends Generator{
   val cpu = new Generator { ... }
   val interconnect = new Generator { ... }
   def addGpio(address : Int, width : Int) = new Generator {
       interconnect.dependencies += this
       add task new Area {
        val peripheral = Apb3Gpio(width)
        interconnect.map(peripheral.io.bus, address, 4 KiB)
        val gpio = master(TriStateArray(width))
        gpio <> ctrl.io.gpio
       }
   }
}

---
There is very much to do !
- New design patterns to invents
  - To squeeze more out of your ASIC/FPGA and our limited man power
  - To make hardware description agile, we aren't coding monkies
- Implementing hardware by using those design patterns
  - CPU, SoC, Interconnect, Peripherals, …
- Emerging HDL to support
  - SpinalHDL, Chisel, Migen, Clash, …

---
In brief, this talk will
- CPU
- Interconnect
- Memories interface
- Peripherals (GPIO, UART, SPI, I2C)
- JTAG (Debug interface)
- DMA

---
RISC-V, in short
- 3 Specs
  - User-Level ISA Specification (RV32I [M] [C] [A] [E])
  - Privileged ISA Specification (Fully optional)
  - Debug Specification (Fully optional)
- 31 words register file + 1 always zero
- Compare-and-branch (no status flag)
- The toolchain is ready to be used
  - But it’s maybe a bit too early for the E extension (15 words register file)
- There is multiple working RTOS ports
  - FreeRTOS
  - Zephyr
  - ...

---
Instruction decoder datamodel
decoderService.add(
 instruction = M"0000000-------000---0110011",
 effect = List(
   ALU_CTRL -> AluCtrlEnum.ADD,
   SRC1_CTRL -> Src1CtrlEnum.RS,
   SRC2_CTRL -> Src2CtrlEnum.IMI,
   REGFILE_WRITE_VALID -> True
   // ...
 )
)

---
CPU pipeline datamodel
insert map
pipeline table
//Global definition of the Programm Counter concept
object PC extends Stageable(UInt(32 bits))
//Somewere in the plugin which manage the program counter
decode.insert(PC) := X
//Somewere in the MachineCsr plugin
Y := writeBack.input(PC)
Key
Value
Index
Stage
PC
X
0
decode
...
...
1
execute
2
memory
input map
3
writeback
Key
Value
PC
Y
...
...