SaxonSoc

---
In short
- Started in parallel to VexRiscv SMP
- Based on
  - SpinalHDL “Generator” tool
  - Banana Memory Bus
- Key features
  - Memory atomics
  - Memory coherency
  - SDR/DDR2/DDR3 controller
  - Multi-core Linux
  - BMB (Memory bus)

---
ArtyA7 port

---
BMB (Banana Memory Bus)
- Goal :
  - Allow both cache-less and cache-full designs (latency / bandwidth)
  - Avoid FPGA expensive interconnects
  - No license of any sort
- Key concepts
  - cmd / rsp streams for accesses
  - cmd.context retrieved in rsp.context
  - [inv / ack / sync] stream for cache invalidation
  - [out of order]

---
Generator example
val a,b = Handle[Int]
//Print a + b
val calculator = new Generator{
   //Specify that this generator need a and b before executing his tasks
   dependencies += a
   dependencies += b
   //Create a new task that will run when all the dependencies are loaded
   add task{
       val sum = a.get + b.get
       println(s"a + b = $sum") //Will print a + b = 7
   }
}
//load a and b with values, which will then unlock the calculator generator
a.load(3)
b.load(4)