VexRiscv

---
In short
- Started in 2017
- Initial goals
  - Modular and extensible hardware description
  - Test and demonstrate SpinalHDL
  - Free open source NIOS II / Microblaze alternative
  - FPGA synthesis friendly
  - Baremetal only
- Current state
  - RV32I[M][A][C][S], recently added [F][D]
  - JTAG via openocd
  - Can run upstream Linux with SMP

---
A standard pipeline

---
But a “empty” toplevel
class VexRiscv(val config : VexRiscvConfig) extends Component with Pipeline{
   type T = VexRiscv
   import config._
   //Define stages
   def newStage(): Stage = { val s = new Stage; stages += s; s }
   val decode = newStage()
   val execute = newStage()
   val memory = ifGen(config.withMemoryStage) (newStage())
   val writeBack = ifGen(config.withWriteBackStage) (newStage())
   def stagesFromExecute = stages.dropWhile(_ != execute)
   plugins ++= config.plugins
    … + 15 lines of stuff related to testing
}

---
val plugins = VexRiscvConfig(
    plugins = List(
       new IBusSimplePlugin(catchAccessFault = false, resetVector = 0x00000000l),
       new DBusSimplePlugin(catchAccessFault = false),
       new DecoderSimplePlugin(catchIllegalInstruction = false),
       new RegFilePlugin,
       new IntAluPlugin,
       new FullBarrielShifterPlugin,
       new HazardSimplePlugin(
        bypassExecute = false,
        bypassMemory = false,
        bypassWriteBack = false
        ),
       new MulPlugin,
       new DivPlugin,
       new MachineCsr(...),
       new BranchPlugin(
        catchAddressMisaligned = false,
        prediction = DYNAMIC
        )
   )
)
val cpu = new VexRiscv(plugins)
Modular CPU framework

---
CPU framework - Connections
//Global definition of the Programm Counter concept
object PC extends Stageable(UInt(32 bits))
//Somewere in the PcManager plugin
fetch.insert(PC) := X
//Somewere in the MachineCsr plugin
Y := writeBack.input(PC)

---
CPU framework - Connections
//Somewhere in the Branch plugin
val jumpInterface = pcPlugin.createJumpInterface(stage = execute)
//Later in the branch plugin
jumpInterface.valid := wannaJump
jumpInterface.payload := execute.input(PC) + execute.input(INSTRUCTION)(31 downto 20)

---
Plugin base class
trait Plugin[T <: Pipeline] extends Nameable{
   // Used to setup things with other plugins
   def setup(pipeline: T) : Unit
   //Used to flush out the required hardware (called after setup)
   def build(pipeline: T) : Unit
   ...
}

---
SIMD add (4 parallel 8 bits add)
class SimdAddPlugin extends Plugin[VexRiscv]{
   object IS_SIMD_ADD extends Stageable(Bool)
   override def setup(pipeline: VexRiscv): Unit = {
      ...
   }
   override def build(pipeline: VexRiscv): Unit = {
        ...
   }
}

---
SIMD add (4 parallel 8 bits add)
    override def setup(pipeline: VexRiscv): Unit = {
       import pipeline.config._
       val decoderService = pipeline.service(classOf[DecoderService])
       decoderService.addDefault(IS_SIMD_ADD, False)
       decoderService.add(
        key = M"0000011----------000-----0110011",
        List(
        IS_SIMD_ADD -> True,
        REGFILE_WRITE_VALID -> True,
        BYPASSABLE_EXECUTE_STAGE -> True,
        BYPASSABLE_MEMORY_STAGE -> True,
        RS1_USE -> True,
        RS2_USE -> True
        )
       )
   }

---
SIMD add (4 parallel 8 bits add)
override def build(pipeline: VexRiscv): Unit = {
     import pipeline._
     import pipeline.config._
     execute plug new Area {
        val rs1 = execute.input(RS1).asUInt
        val rs2 = execute.input(RS2).asUInt
        val rd = UInt(32 bits)
        rd(7 downto 0) := rs1( 7 downto 0) + rs2( 7 downto 0)
        rd(16 downto 8) := rs1(16 downto 8) + rs2(16 downto 8)
        rd(23 downto 16) := rs1(23 downto 16) + rs2(23 downto 16)
        rd(31 downto 24) := rs1(31 downto 24) + rs2(31 downto 24)
        when(execute.input(IS_SIMD_ADD)) {
        execute.output(REGFILE_WRITE_DATA) := rd.asBits
        }
    }
}

---
Many plugins
AesPlugin.scala IntAluPlugin.scala
BranchPlugin.scala MemoryTranslatorPlugin.scala
CfuPlugin.scala Misc.scala
CsrPlugin.scala MmuPlugin.scala
DBusCachedPlugin.scala Mul16Plugin.scala
DBusSimplePlugin.scala MulDivIterativePlugin.scala
DebugPlugin.scala MulPlugin.scala
DecoderSimplePlugin.scala MulSimplePlugin.scala
DivPlugin.scala NoPipeliningPlugin.scala
DummyFencePlugin.scala PcManagerSimplePlugin.scala
ExternalInterruptArrayPlugin.scala Plugin.scala
Fetcher.scala PmpPlugin.scala
FormalPlugin.scala RegFilePlugin.scala
FpuPlugin.scala ShiftPlugins.scala
HaltOnExceptionPlugin.scala SingleInstructionLimiterPlugin.scala
HazardPessimisticPlugin.scala SrcPlugin.scala
HazardSimplePlugin.scala StaticMemoryTranslatorPlugin.scala
IBusCachedPlugin.scala YamlPlugin.scala
IBusSimplePlugin.scala

---
DataCache features
- Write-through
- Atomic via load reserve and store conditional
- Coherency via invalidation
- Multi way, no more than 4KB per way if the MMU is used
- Flexible refill data width

---
Other features to setup
- Multiplication : Iterative in 32/2^n cycles | single cycle 17x17x4
- Register file : Sync | Async read, X0 init kind
- Branch : Prediction, late
- Hazard : Interlock | bypass
- Fetch : pipelining levels, RVC
- Memory, Writeback : can be optional
- Many other timings related things