An alternative hardware description language

---
Summary
- VHDL and Verilog are not so good
- SpinalHDL introduction
- Examples
- Disclamer
  - This talk will only be about synthesizable hardware

---
VHDL and Verilog
- Initialy designed for simulation/documentation purposes, a long time ago
  - Process/Always blocks doesn't make sense in RTL
  - No object oriented programming, no functional programming
- Simple concepts are verbose
  - Component/Module instanciation
  - Interface instanciation
- No meta-hardware description capabilites

---
Blessed VHDL-2008 and SV ?
- Not realy
  - They keep the same paradigm to infer RTL (simulation constructs)
  - They didn't offer any meta-hardware description capabilities
  - VHDL-2008 Synthesis support could be realy bad
  - SV interface definitions are limited

---
VHDL-2002 and Verilog-2005 issues
- Process/Always blocks are counter productive for RTL
- High verbosity (ex : Component instanciation)
- Using generics exclude the usage of records and arrays in the entity
- No interface definition concepts (ex APB, AHB, Avalon, AXI, Wishbone)
- Function and procedures are quite limited

---
Blessed VHDL-2008 and SV ?
- Not realy
  - They keep the same paradigm to infer RTL (simulation constructs)
  - They didn't offer any meta-hardware description capabilities
  - VHDL-2008 Synthesis support could be realy bad
  - SV interface definitions are limited

---
Mythology
- Synthesizable subset and EDA support
  - VHDL buffer keyword ?
  - VHDL ranged access on vector ?
  - VHDL time in generics ?
  - VHDL and Verilog zero width vector ?
  - VHDL variable ?
  - VHDL record ?
  - VHDL read text file ?
  - SystemVerilog two dimentional array of interface ?

---
So, what to do next ?
Use VHDL and Verilog as netlist language !
Source: SonicBomb.com galleries

---
SpinalHDL introduction
- Open source , started in december 2014
- Focus on RTL description
- Thinked to be interoperable with existing tools
  - It generates VHDL/Verilog files (as an output netlist)
  - It can integrate VHDL/Verilog IP as blackbox
Abstraction level :
  - You can design things similary to VHDL/Verilog
  - If you want to, you can use many abstraction utils and also define new ones

---
Some points about SpinalHDL
- There is no logic overhead in the generated code. (I swear !)
- The component hierarchy and all names are preserved during the VHDL/Verilog generation. (Good for simulations)
- It is an language hosted on the top of Scala ! (And it is a very good thing)

---
By using events driven constructs (VHDL)
    signal mySignal : std_logic;
   process(cond)
   begin
       mySignal <= '0';
       if cond = '1' then
        mySignal <= '1';
       end if;
   end process;
    signal myRegister : unsigned(3 downto 0);
    process(clk)
   begin
       if rising_edge(clk) then
        if cond = '1' then
        myRegister <= myRegister + 1;
        end if;
       end if;
   end process;
    signal myRegisterWithReset : unsigned(3 downto 0);
    process(clk,reset)
    begin
       if reset = '1' then
        myRegisterWithReset <= 0;
       elsif rising_edge(clk) then
        if cond = '1' then
        myRegisterWithReset <= myRegisterWithReset + 1;
        end if;
       end if;
   end process;
[Speaker Notes: In VHDL you need to split the logic between combinatoral / sequancial with reset / sequancial without reset]

---
By using an dedicated syntax (SpinalHDL)
val mySignal = Bool
val myRegister = Reg(UInt(4 bits))
val myRegisterWithReset = Reg(UInt(4 bits)) init(0)
mySignal := False
when(cond) {
   mySignal := True
   myRegister := myRegister + 1
   myRegisterWithReset := myRegisterWithReset + 1
}
SpinalHDL => 9 lines
VHDL => 28 lines
[Speaker Notes: In VHDL you need to split the logic between combinatoral / sequancial with reset / sequancial without reset]

---
ClockDomains
val coreClk = Bool
   val coreReset = Bool
val coreClockDomain = ClockDomain(
       clock = coreClk,
       reset = coreReset,
       config = ClockDomainConfig(
        clockEdge = RISING,
        resetKind = ASYNC,
        resetActiveLevel = HIGH
       )
   )
   val coreArea = new ClockingArea(coreClockDomain) {
       val myCoreClockedRegister = Reg(UInt(4 bit))
       //...
   }

---
Real functions capabilities
// Input RGB color
val r,g,b = UInt(8 bits)
// Define a function to multiply a UInt by a scala Float value.
def coefMul(value : UInt,by : Float) : UInt = {
   val resultReg = Reg(UInt(8 bits))
   resultReg := (value * U((255*by).toInt,8 bits)) >> 8
   return resultReg
}
//Calculate the gray level
val gray = coefMul(r, 0.3f) +
        coefMul(g, 0.4f) +
        coefMul(b, 0.3f)
[Speaker Notes: In VHDL you can’t create a function that assign combinatoral and sequancial logic]

---
Having a Hand-shake bus of color and wanting to queue it ?
[Speaker Notes: In VHDL you need to split the logic between combinatoral / sequancial with reset / sequancial without reset]

---
In standard VHDL
    fifo_inst : entity work.Fifo
        generic map (
        depth => 16,
        payload_width => 16
        )
        port map (
        clk => clk,
        reset => reset,
        push_valid => source_valid,
        push_ready => source_ready,
        push_payload(4 downto 0) => source_payload_r,
        push_payload(10 downto 5) => source_payload_g,
        push_payload(15 downto 11) => source_payload_b,
        pop_valid => sink_valid,
        pop_ready => sink_ready,
        pop_payload(4 downto 0) => sink_payload_r,
        pop_payload(10 downto 5) => sink_payload_g,
        pop_payload(15 downto 11) => sink_payload_b
        );
    signal source_valid : std_logic;
    signal source_ready : std_logic;
    signal source_r : unsigned(4 downto 0);
    signal source_g : unsigned(5 downto 0);
    signal source_b : unsigned(4 downto 0);
    signal sink_valid : std_logic;
    signal sink_ready : std_logic;
    signal sink_r : unsigned(4 downto 0);
    signal sink_g : unsigned(5 downto 0);
    signal sink_b : unsigned(4 downto 0);
[Speaker Notes: In VHDL you need to split the logic between combinatoral / sequancial with reset / sequancial without reset]

---
In SpinalHDL
val source, sink = Stream(RGB(5,6,5))
val fifo = StreamFifo(
   dataType = RGB(5,6,5),
   depth = 16
)
fifo.io.push << source
fifo.io.pop >> sink
SpinalHDL => 7 lines
VHDL => 29 lines
[Speaker Notes: In VHDL you need to split the logic between combinatoral / sequancial with reset / sequancial without reset]

---
About RGB
case class RGB( rWidth : Int,
        gWidth : Int,
        bWidth : Int) extends Bundle{
   val r = UInt(rWidth bits)
   val g = UInt(gWidth bits)
   val b = UInt(bWidth bits)
}
[Speaker Notes: In VHDL you need to split the logic between combinatoral / sequancial with reset / sequancial without reset]

---
About Stream
case class Stream[T <: Data](payloadType : HardType[T]) extends Bundle with IMasterSlave{
   val valid = Bool
   val ready = Bool
   val payload = payloadType()
   override def asMaster(): Unit = {
       out(valid,payload)
       in(ready)
   }
   def >>(sink: Stream[T]): Unit ={
       sink.valid := this.valid
       this.ready := sink.ready
       sink.payload := this.payload
   }
   def <<(source: Stream[T]): Unit = source >> this
    def queue(depth : Int) : Stream[T] = {...}
}
Stream(RGB(5,6,5))
[Speaker Notes: In VHDL you need to split the logic between combinatoral / sequancial with reset / sequancial without reset]

---
Queuing in SpinalHDL++
val source, sink = Stream(RGB(5,6,5))
val fifo = StreamFifo(
   dataType = RGB(5,6,5),
   depth = 16
)
fifo.io.push << source
fifo.io.pop >> sink
val source, sink = Stream(RGB(5,6,5))
source.queue(16) >> sink
SpinalHDL => 2 lines
VHDL => 29 lines
[Speaker Notes: In VHDL you need to split the logic between combinatoral / sequancial with reset / sequancial without reset]

---
Queuing in SpinalHDL++
case class RGB( rWidth : Int,
        gWidth : Int,
        bWidth : Int) extends Bundle{
   val r = UInt(rWidth bits)
   val g = UInt(gWidth bits)
   val b = UInt(bWidth bits)
    def isBlack : Bool = (r === 0 && g === 0 && b === 0)
}
val source = Stream(RGB(5,6,5))
val sink = source.throwWhen(source.payload.isBlack).stage()
SpinalHDL => 2 lines
VHDL => Sorry, I'm too lazy
[Speaker Notes: In VHDL you need to split the logic between combinatoral / sequancial with reset / sequancial without reset]

---
Safty first !
val a = Bool
   val result = Bool
result := a | result //Loop detected by SpinalHDL
val result = Bool
when(cond){ //result is not assigned in all cases => Latch detected by SpinalHDL
       result := True
   }
[Speaker Notes: Spinal check if there is combinatorial loop and print a error when one is detected.]

---
Basic abstractions
val timeout = Timeout(1000)
when(timeout){ //implicit conversion to Bool
   timeout.clear() //Clear the flag and the internal counter
}
//Create a counter of 10 states (0 to 9)
val counter = Counter(10)
counter.clear() //When called it reset the counter. It's not a flag
counter.increment() //When called it increment the counter. It's not a flag
counter.value //current value
counter.valueNext //Next value
counter.willOverflow //Flag that indicate if the counter overflow this cycle
when(counter === 5){ …}
[Speaker Notes: Some basics abstraction are defined in the Spinal Lib.]

---
Functional programming
val addresses = Vec(UInt(8 bits),4)
val key = UInt(8 bits)
val hits = addresses.map(address => address === key)
val hit = hits.reduce((a,b) => a || b)

---
Design introspection
val a = UInt(8 bits)
val b = UInt(8 bits)
val aCalcResult = complicatedLogic(a)
val aLatency = LatencyAnalysis(a,aCalcResult)
val bDelayed = Delay(b,cycleCount = aLatency)
val result = aCalcResult + bDelayed
[Speaker Notes: Because spinal build a netlist in the memory, you can use it to extract some information, for example latency (in cycle) between some points of you design. To do that, call LatencyAnalysis and give to it as argument some the start point, some check point and the end point of you path. It look for the shortest path and return how many cycle there is.]

---
Meta-hardware description examples

---
FSM
- They could be defined with regular syntax (Enum,Switch)
- You can also use a much more friendly syntax, fully integrated, with following features :
  - onEntry / onExit / whenIsActive / whenIsNext blocs
  - State with inner FSM
  - State with multiple inner FSM (parallel execution)
  - Delay state
  - You can extends the syntax by defining new state types

---
FSM
val fsm = new StateMachine{
   val stateA = new State with EntryPoint
   val stateB = new State
   val stateC = new State
   val counter = Reg(UInt(8 bits)) init (0)
   io.result := False
   stateA
       .whenIsActive (goto(stateB))
   stateB
       .onEntry(counter := 0)
       .whenIsActive {
        counter := counter + 1
        when(counter === 4){
        goto(stateC)
        }
       }
       .onExit(io.result := True)
   stateC
       .whenIsActive (goto(stateA))
}
val io = new Bundle{
   val result = out Bool
}

---
JTAG slave (tap)
class SimpleJtagTap extends Component {
   val io = new Bundle {
       val jtag = slave(Jtag())
       val switchs = in Bits(8 bit)
       val leds = out Bits(8 bit)
   }
   val tap = new JtagTap(io.jtag, 8)
   val idcodeArea = tap.idcode(B"x87654321")(instructionId=4)
   val switchsArea = tap.read (io.switchs) (instructionId=5)
   val ledsArea = tap.write(io.leds) (instructionId=6)
}

---
Imagine a simple timer
case class Timer(width : Int) extends Component{
   val io = new Bundle{
       val tick = in Bool
       val clear = in Bool
       val limit = in UInt(width bits)
       val full = out Bool
       val value = out UInt(width bits)
   }
   val counter = Reg(UInt(width bits))
   when(io.tick && !io.full){
       counter := counter + 1
   }
   when(io.clear){
       counter := 0
   }
   io.full := counter === io.limit
   io.value := counter
}

---
Imagine you want to connect it

---
Bus Slave Factory
- OOP meet Hardware description !
- BusSlaveFactory implementations are able to create register banks by using an abstract way. Let’s use it to bind our Timer !

---
Let's define a function !
case class Timer(width : Int) extends Component{
     val io = new Bundle {
        // …
        def driveFrom(busCtrl : BusSlaveFactory,baseAddress : BigInt)
        (ticks : Seq[Bool],clears : Seq[Bool]) = new Area {
        clear := False
        //Address 0 => read/write limit (+ auto clear)
        busCtrl.driveAndRead(limit,baseAddress + 0)
        clear.setWhen(busCtrl.isWriting(baseAddress + 0))
        //Address 4 => read timer value / write => clear timer value
        busCtrl.read(value,baseAddress + 4)
        clear.setWhen(busCtrl.isWriting(baseAddress + 4))
        //Address 8 => clear/tick masks + bus
        // ...
        }
     }
     // …
}

---
Let's use it :
val prescalerBridge = prescaler.io.driveFrom(busCtrl,0x00)
val timerABridge = timerA.io.driveFrom(busCtrl,0x40)(
   ticks = List(True, prescaler.io.overflow),
   clears = List(timerA.io.full)
)
val timerBBridge = timerB.io.driveFrom(busCtrl,0x50)(
   ticks = List(True, prescaler.io.overflow, external.tick),
   clears = List(timerB.io.full, external.clear)
)
val timerCBridge = timerC.io.driveFrom(busCtrl,0x60)(
   ticks = List(True, prescaler.io.overflow, external.tick),
   clears = List(timerC.io.full, external.clear)
)
val apb = Apb3(addressWidth = 8, dataWidth = 32)
val external = new Bundle{
   val clear,tick = Bool
}
val prescaler = Prescaler(16)
val timerA = Timer(32)
val timerB,timerC = Timer(16)
val busCtrl = Apb3SlaveFactory(apb)

---
Spinal works perfectly on FPGA
RISCV CPU, 5 stages
  - MUL/DIV
  - Instruction/Data cache
  - Interrupts
  - JTAG debugging
- AXI/APB interconnect
- Avalon/APB UART
- Avalon/AXI VGA
- Pipelined and multi-core fractal accelerator

---
Pinsec SoC

---
Peripheral side
val apbBridge = Axi4ToApb3Bridge(
   addressWidth = 20,
   dataWidth = 32,
   idWidth = 4
)
val apbDecoder = Apb3Decoder(
   master = apbBridge.io.apb,
   slaves = List(
       gpioACtrl.io.apb -> (0x00000, 4 kB),
       gpioBCtrl.io.apb -> (0x01000, 4 kB),
       uartCtrl.io.apb -> (0x10000, 4 kB),
       timerCtrl.io.apb -> (0x20000, 4 kB),
       vgaCtrl.io.apb -> (0x30000, 4 kB),
       core.io.debugBus -> (0xF0000, 4 kB)
   )
)

---
AXI4 side (OOP builder pattern)
val axiCrossbar = Axi4CrossbarFactory()
axiCrossbar.addSlaves(
   ram.io.axi -> (0x00000000L, onChipRamSize),
   sdramCtrl.io.axi -> (0x40000000L, sdramLayout.capacity),
   apbBridge.io.axi -> (0xF0000000L, 1 MB)
)
axiCrossbar.addConnections(
   core.io.i -> List(ram.io.axi, sdramCtrl.io.axi),
   core.io.d -> List(ram.io.axi, sdramCtrl.io.axi, apbBridge.io.axi),
   jtagCtrl.io.axi -> List(ram.io.axi, sdramCtrl.io.axi, apbBridge.io.axi),
   vgaCtrl.io.axi -> List( sdramCtrl.io.axi)
)
axiCrossbar.build()

---
About Scala
Free Scala IDE (eclipse, intelij)
  - Highlight syntax error
  - Renaming flexibility
  - Intelligent auto completion
  - Code structure overview
  - Navigation tools
- Emacs plugin
- Allow you to extend the language
- Provide many libraries

---
About SpinalHDL project
Completely open source :
    - https://github.com/SpinalHDL/SpinalHDL
Online documentation :
    - https://spinalhdl.github.io/SpinalDoc/
Ready to use base project :
    - https://github.com/SpinalHDL/SpinalBaseProject
Communication channels :
    - spinalhdl@gmail.com
    - https://gitter.im/SpinalHDL/SpinalHDL
    - https://github.com/SpinalHDL/SpinalHDL/issues

---
End / reserve slides