Basics and VHDL/Verilog Equivalences

---
Types
SpinalHDL	VHDL	Verilog
Bool()	std_logic
Bits(8 bits)	std_logic_vector(7 downto 0)	[7:0]
UInt(8 bits)	unsigned(7 downto 0)	unsigned [7:0]
SInt(8 bits)	signed(7 downto 0)	signed [7:0]
Bundle	record	struct
Vec(SInt(8 bits), 4)	array(0 to 4) of signed(7 downto 0)	signed [7:0] … [0:3]
Data	-	-
[Speaker Notes: In VHDL you need to split the logic between combinatoral / sequancial with reset / sequancial without reset]

---
Arithmetics returned width
Operator kind	Examples	Returned width
Boolean	&& || === =/=	1 (Bool)
Bitwise	& | ^	left, right (both width should match)
Add Sub	+ -	max(left, right)
Mult	*	left + right
Shift with width changes	>> <<	left +- maximum shift amount
Shift with fixed width	|>> |<<	left
[Speaker Notes: In VHDL you need to split the logic between combinatoral / sequancial with reset / sequancial without reset]

---
Assignements
Operator kind	Description
val x = UInt(8 bits)	Scala constant reference declaration
x := y	Hardware assignement (like <= in VHDL/Verilog)
var y = Uint(8 bits)	Scala variable reference declaration
y = x	Scala reference assignement
y \= x	Hardware assignement (like variable in VHDL and = in Verilog)
[Speaker Notes: In VHDL you need to split the logic between combinatoral / sequancial with reset / sequancial without reset]

---
Semantic
val counter = Reg(UInt(8 bits))
when(something){
   counter := counter + 1
}
when(clearFlag){
   counter := 0
}
val result = UInt(8 bits)
result := 0
when(something){
   result := 42
   when(somethingElse){
       result := 0xEE
   }
}
- Constructing hardware by
  - Instanciating things
  - Defining rules
  - Last rule win
  - Using implicit clock domains
when(softReset){
   counter := 0
   result := 0x88
}
// forward reference => result is null => error
x := result
val result = UInt(8 bits)
Conditional scope can be used by combinatorial and register assignements !
[Speaker Notes: In VHDL you need to split the logic between combinatoral / sequancial with reset / sequancial without reset]

---
Variable
val a = UInt (size bits)
   val b = UInt (size bits)
   val result = UInt (size bits)
   var c = False
   for (i <- 0 until size) {
       val x = io.a(i)
       val y = io.b(i)
       io.result(i) := x ^ y ^ c
       c \= (x & y) | (x & c) | (y & c);
   }
[Speaker Notes: In VHDL you need to split the logic between combinatoral / sequancial with reset / sequancial without reset]

---
OOP rules apply there
x := result // forward reference => result is null => error
val result = UInt(8 bits)
[Speaker Notes: In VHDL you need to split the logic between combinatoral / sequancial with reset / sequancial without reset]

---
Literals
but not only
val myBool = False
when(something){
   myBool := True
}
val myBool = Bool()
myBool := False
myBool := True
val myUInt = UInt(8 bits)
myUInt := "0001_1100"
myUInt := "xEE"
myUInt := 42
myUInt := 0x42
myUInt := U(54, 8 bits)
myUInt := ((3 downto 0) -> myBool,default -> true)
when(myUInt === U(myUInt.range -> true)){
   myUInt(3) := False
}
val myConstant = U"0001_1100"
process(something)
begin
  myBool <= '0';
  if something = '1' then
      myBool <= '1';
  end if;
end process;
Bits
Bits
Bits
Bits
Bits
Bits
UInt
UInt
UInt
SInt
SInt
SInt

---
Type manipulations
val uint8 = UInt(8 bits)
val uint12 = UInt(12 bits)
uint8 := uint12 //Error
uint12 := uint8 //Error
uint8 := uint12.resize(8)
uint8 := uint12.resized
uint8 := uint12(7 downto 0)
uint8 := uint12(uint8.range)
val bits4 = Bits(4 bits)
uint8 := bits4.asUInt.resized
case class RGB(channelWidth : Int) extends Bundle{
   val r,g,b = UInt(channelWidth bits)
}
val bitsIn, bitsOut = Bits(12 bits)
val color = RGB(4)
color.assignFromBits(bitsIn)
bitsOut := color.asBits
Bits
Bits
Bits
Bits
Bits
Bits
UInt
UInt
UInt
SInt
SInt
SInt

---
Component / Entity / Architecture / Module
import spinal.core._
class Adder(width : Int) extends Component{
   val io = new Bundle {
       val a,b = in UInt(width bits)
       val result = out UInt(width bits)
   }
   val a_add_b = UInt(width bits)
   a_add_b := io.a + io.b
   io.result := a_add_b
}
library ieee;
use ieee.std_logic_1164.all;
use ieee.numeric_std.all;
entity Adder is
 generic (
   width : integer
 );
 port(
   io_a : in unsigned(width-1 downto 0);
   io_b : in unsigned(width-1 downto 0);
   io_result : out unsigned(width-1 downto 0)
 );
end Adder;
architecture arch of Adder is
 signal a_add_b : unsigned(width-1 downto 0);
begin
 io_result <= a_add_b;
 a_add_b <= io_a + io_b;
end arch;
module Adder #(parameter width) (
   input [width-1:0] io_a,
   input [width-1:0] io_b,
   output [width-1:0] io_result
 );
 wire [width-1:0] a_add_b;
 assign a_add_b = (io_a + io_b);
 assign io_result = a_add_b;
endmodule
[Speaker Notes: In VHDL you need to split the logic between combinatoral / sequancial with reset / sequancial without reset]

---
No component binding required, access things in a OOP manner
class Adder(width : Int) extends Component{
 val io = new Bundle {
   val a,b = in UInt(width bits)
   val result = out UInt(width bits)
 }
 val a_add_b = UInt(width bits)
 a_add_b := io.a + io.b
 io.result := a_add_b
}
val adder8 = new Adder(8)
adder8.io.a := 21
adder8.io.b := ???
when(adder8.io.result > 32){
  //...
}
[Speaker Notes: In VHDL you need to split the logic between combinatoral / sequancial with reset / sequancial without reset]

---
Function and namespaces
val isZero = Bool()
val shifted = UInt(9 bits)
val square = UInt(16 bits)
def load(value : UInt) : Unit = {
   require(widthOf(value) == 8)
   isZero := value === 0
   shifted := value << 1
   square := value * value
}
when(something){
   load(U"1110_0000")
} otherwise {
   load(U"0010_0010")
}
val landaLogic = new Area{
   val a,b = UInt(8 bits)
   val result = a + b
   val flag = False
}
val somethereElse = new Area{
   val flag = False || landaLogic.result.lsb
}
when(landaLogic.result === 88){
   somethereElse.flag := False
}
[Speaker Notes: In VHDL you need to split the logic between combinatoral / sequancial with reset / sequancial without reset]

---
More documentation online
https://spinalhdl.github.io/SpinalDoc/