SpinalHDL : Software generated hardware
But let's name this presentation another way :
  - Hardware description API (HDAPI) paradigm
(HDAPI will refer to nothing on search engines)

---
Hardware description API (HDAPI) paradigm
- Populating an netlist by using a library API (ex : SpinalHDL)
- Using the general purpose capabilities of the host language (ex : Scala) to elaborate/structurate the design
val reg1 = Reg(UInt(8 bits))
val cond = reg1 === 42
VHDL/Verilog
val reg2 = Reg(UInt(8 bits)) init(0)
when(cond){
 reg2 := 50
}

---
The SpinalHDL hardware API
- Hardware types (Bool, Bits, UInt, SInt, Bundle, Vec, …)
- Hardware conditional statements (when, switch)
- Hardware operators (:=, + - * / %, && || ^ ~, ...)
- And few others hardware constructs (Component, in, out, Area, ClockDomain, …)
- All the scala features can be used to elaborate the netlist
  - Scala types : Int, String, Float, ..
  - Scala conditional statements : if, match
  - Scala constructs : class, def, val, var, for, ...

---
Just some points before continuing
- About SpinalHDL
  - There is no logic overhead in the RTL, as everything is explicit
  - Will give you an error message instead of generating broken/not synthesizable VHDL/Verilog
    - No latches, no combinatorial loop, no signal width mismatch, …
  - SpinalHDL isn't a language, it's a HDAPI in Scala
- But this talk isn't realy about SpinalHDL
  - It will not introduce much of the SpinalHDL syntax
  - It will focus on giving you keys example to “feel” some of the potential of HDAPI (SpinalHDL, Chisel, FHDL, …)

---
Semantic example
Red => SpinalHDL netlist API
Everything else is Scala
//**Implementation via function/reference**
val condA, condB = Bool()
val result = UInt(8 bits)
result := 0
//Function call will be inlined in the netlist
whenAssign(condA, result, 42)
whenAssign(condB, result, 255)
def whenAssign(condition: Bool, target: UInt, value: UInt) = {
   when(condition) {
       target := value
   }
}
//**Standard implementation**
val condA, condB = Bool()
val result = UInt(8 bits)
result := 0
when(condA) {
   result := 42
}
when(condB) {
   result := 255
}
Scala

---
Semantic example
Red => SpinalHDL netlist API
Everything else is Scala
//**Generation via a datamodel**
val condA, condB = Bool()
val result = UInt(8 bits)
result := 0
val spec = ArrayBuffer[(Bool, UInt)]() //(X,Y) is a scala tuples
spec += condA -> 42 //Tuples can be created with x -> y syntax
spec += condB -> 255
//Loop iterations will be inlined in the netlist
for((cond, value) <- spec){
   when(cond){
       result := value
   }
}
//**Standard implementation**
val condA, condB = Bool()
val result = UInt(8 bits)
result := 0
when(condA) {
   result := 42
}
when(condB) {
   result := 255
}
Scala

---
Dynamic list & memory mapping
val apbMapping = ArrayBuffer[(Apb3, SizeMapping)]()
val gpioA = Apb3Gpio(gpioWidth = 32)
apbMapping += gpioA.io.apb -> (0x0000, 4 kB)
val gpioB = Apb3Gpio(gpioWidth = 16)
apbMapping += gpioB.io.apb -> (0x1000, 4 kB)
if(genGpioC) {
   val gpioC = Apb3Gpio(gpioWidth = 8)
   apbMapping += gpioC.io.apb -> (0x2000, 4 kB)
}
val apbDecoder = Apb3Decoder(
   master = apbBridge.io.apb,
   slaves = apbMapping
)
Similarly, this approach can be used for the interrupt controller mapping

---
State machine meta model
class StateMachine{
   val states = ArrayBuffer[State]()
   var initialState : State = null
   var stateReg, stateNext : UInt = null
    def goto(target : State) = { ... }
   def build(): Unit = { … }
}
- The StateMachine has :
  - Multiple states
  - One of them is the initial state
  - One register which store the current state
  - One signal to set the next state
- The States has :
  - A given hardware identifier
  - Actions when active, on entry, on exit
class State(){
   var id : UInt = null
    // The () => Unit type is a reference to a
    // argument/return less function
   var activeAction : () => Unit = null
   var entryAction : () => Unit = null
   var exitAction : () => Unit = null
}

---
def build(): Unit ={
   //Give a hardware identifier to all states (states encoding)
   for(i <- 0 until states.length) states(i).id = U(i)
   //Create the state register/signal of the state machine and interconnect them
   stateReg = Reg(UInt(log2Up(states.length) bits)) init(initialState.id)
   ...
   //Generate the hardware for whenActive + exitActions
   switch(stateReg){
     for(state <- states){
        is(state.id){
        if(state.activeAction != null) { state.activeAction() }
        if(state.exitAction != null) {
        when(stateNext =/= state.id){
        state.exitAction()
        }
        }
        }
       }
   }
    ...
}
class StateMachine{
   val states = ArrayBuffer[State]()
   var initialState : State = null
   var stateReg, stateNext : UInt = null
    def goto(target : State) = { stateNext := target.id }
   def build(): Unit = { … }
}

---
State machine example
val fsm = new StateMachine{
   val stateA, stateB = new State()
   val counter = Reg(UInt(8 bits))
   stateA.entryAction = (){ counter := 0 }
   stateA.activeAction = (){
       counter := counter + 1
       when(counter === 4){
        goto(stateB)
       }
   }
   …
  build()
}

---
State machine generator can be regarded as overkill, but :
- You can define new states kind as :
- You can also create custom StateMachine generators
  - Secure/special encoding
  - Integrated debuging feature
- You can algorithmically add/remove states via if/for/scala to your FSM
- We just added a hardware description abstraction layer
//Create a state which will wait 30 cycles before going to stateY
val stateX = StateDelay(30, stateY)
//Create a state which will run two sub state machine before going to stateX
val stateY = StateParallelFsm (fsmA, fsmB, stateX)

---
Simple peripheral design
- Let's imagine a simple peripheral which do XOR operations
  - We want to access it from a memory bus
  - So we need to create a bridge between the memoryBus and the peripheral signals (a, b, result)
- But first, let's create a memory mapping tool.

---
Memory mapping meta model
abstract class MemoryMapper{
 val spec = HashMap[Int, ArrayBuffer[Any]]()
 def write(target : Bits, address : Int) = spec(address) += WriteAccess(target)
 def read(source : Bits, address : Int) = spec(address) += ReadAccess(source)
 def drive(target : Bits, address : Int) = {
   val reg = Reg(Bits(widthOf(target) bits))
   write(reg, address)
   target := reg
 }
 def build()
}
case class WriteAccess(target : Bits)
case class ReadAccess(source : Bits)

---
Memory mapping APB3 implementation
class ApbMemoryMapper(bus : Apb3) extends MemoryMapper{
   override def build(): Unit = {
        ...
       val doWrite = bus.PSEL(0) && bus.PENABLE && bus.PREADY && bus.PWRITE
       switch(bus.PADDR) {
        for ((address, jobs) <- spec) {
        is(address) {
        for(job <- jobs) job match {
        case w : WriteAccess => when(doWrite) { w.target := bus.PWDATA }
        case r : ReadAccess => bus.PRDATA := r.source
        }
        }
        }
       }
   }
}

---
Memory mapping APB3 implementation
val a, b = Bits(32 bits)
val result = a ^ b
//Create a new APB3 bus
val memoryBus = Apb3(addressWidth = 8, dataWidth = 32)
//Create the factory which creates the bridging logic between the bus and some hardware
val memoryMapper = new ApbMemoryMapper(memoryBus)
//Drive 'a' and 'b' from the memoryBus
memoryMapper.drive(target=a, address = 0x00)
memoryMapper.drive(target=b, address = 0x04)
//Make 'result' readable by memoryBus
memoryMapper.read(source=result, address = 0x08)

---
Memory mapping : Abstract class, like in software
- You can create new child classes to support new memory buses !
- You can abstractly define the memory mapping of your peripheral
  - Allow to connect a peripheral to all kind of busses using a single specification
class Something extends Bundle{
   val a, b = UInt(32 bits)
   def driveFrom(factory : MemoryMapper) = new Area {
       factory.drive(a, address = 0x00)
       factory.drive(b, address = 0x04)
   }
}

---
TODO Data model appliyed to other cases
- Pipeline/dataflow
- CPU status register
- Instruction decoder
- JTAG slave

---
The end, tips to think about all of this
- SpinalHDL is a hardware description API, not a language, it never parse your code as a compiler
- When you execute the scala code, each SpinalHDL API call will add information in the SpinalHDL netlist
- All the elaborated features come from Scala (host general purpose language)
- None of the previous slide require SpinalHDL modifications, they are all implemented in RAW SpinalHDL/Scala

---
Some links
- SpinalHDL library sources :
  - https://github.com/SpinalHDL/SpinalHDL
- Online documentation :
  - https://spinalhdl.github.io/SpinalDoc/
- Ready to use base project :
  - https://github.com/SpinalHDL/SpinalTemplateSbt
- Communication channels :
  - spinalhdl@gmail.com
  - https://gitter.im/SpinalHDL/SpinalHDL
  - https://github.com/SpinalHDL/SpinalHDL/issues

---
My profile
- I'm a hardware guy
- I was in love with VHDL and she gived me many hardware babies during 5 years
- Then I meet Scala, and after some black magic surgery, she realy gived me nice, cut and fluffy babies. At this moment, I realised how sick and dirty were my VHDL babies, so, that was the turning point of my life.
- I'm happy now

---
Netlist elaboration features
- Most commonly used in VHDL/Verilog :
  - If then, switch case
  - for loop, for generate, if generate
- Software used as an netlist elaboration tool ?
  - Dynamic lists
  - Dictionnary, Map, Set
  - Abstract class, interface
  - Function and Object reference as a function argument