 From the RISC-V spec to a low-tech SoC
passing by SpinalHDL, VexRiscv and OpenOCD
FSiC, 2019

---
In short about me
- I’m involved into
  - SpinalHDL (Hardware description library)
  - VexRiscv (RISC-V CPU)

---
What it take to implement a SoC netlist from scratch
- CPU
- Interconnect
- Memories interface
- Peripherals (GPIO, UART, SPI, I2C)
- JTAG (Debug interface)
- DMA

---
CPU : RISC-V
- 3 Specs
  - User-Level ISA Specification (RV32I [M] [C] [A] [E])
  - Privileged ISA Specification (Fully optional)
  - Debug Specification (Fully optional)

---
CPU : RISC-V in short
- 3 Specs
  - User-Level ISA Specification (RV32I [M] [C] [A] [E])
  - Privileged ISA Specification (Fully optional)
  - Debug Specification (Fully optional)
- 31 words register file + 1 always zero
- Compare-and-branch (no status flag)
- The toolchain is ready to be used
  - But it’s maybe a bit too early for the E extension (15 words register file)
- There is multiple working RTOS ports
  - FreeRTOS
  - Zephyr
  - ...

---
CPU : VexRiscv
- RV32I[M][C]
- From 2 stages to 4 + X fetch stages
- Implemented in SpinalHDL
  - Elaboration capabilities of VHDL/SystemVerilog are way too limited
  - Automated instruction decoding generation (Quine–McCluskey)
  - Automated pipelining
  - CPU composability and customisation (The parametrization hold the behaviour)

---
SpinalHDL, yet another HDL ...
- Not a even driven language
- Not a High Level Synthesis (HLS)
- Not a data flow language
- Not a language
- A hardware description library (SpinalHDL) implemented in a general purpose programming language (Scala)
- The hardware netlist is elaborated from the software runtime, not a compilation.

---
  BLUE => Software elaboration
  RED => Hardware netlist interaction
  val a,b,c = Reg(UInt(Random.nextInt(10) bits))
  val sum = List(a,b,c).filter(widthOf(_) == 4).reduce(_ + _)

---
Plugin example : 4x8bits add (SIMD)
class SimdAddPlugin extends Plugin[VexRiscv]{
   override def setup(pipeline: VexRiscv): Unit = {
       ...
   }
   override def build(pipeline: VexRiscv): Unit = {
       ..
   }
}

---
class SimdAddPlugin extends Plugin[VexRiscv]{
   object IS_SIMD_ADD extends Stageable(Bool)
   override def setup(pipeline: VexRiscv): Unit = {
       val decoderService = pipeline.service(classOf[DecoderService])
       decoderService.addDefault(IS_SIMD_ADD, False)
       decoderService.add(
        key = M"0000011----------000-----0110011",
        List(
        IS_SIMD_ADD -> True,
        REGFILE_WRITE_VALID -> True,
        BYPASSABLE_EXECUTE_STAGE -> True,
        BYPASSABLE_MEMORY_STAGE -> True,
        RS1_USE -> True,
        RS2_USE -> True
        )
       )
   }
   override def build(pipeline: VexRiscv): Unit = { .. }
}

---
class SimdAddPlugin extends Plugin[VexRiscv]{
   object IS_SIMD_ADD extends Stageable(Bool)
   override def setup(pipeline: VexRiscv): Unit = { .. }
   override def build(pipeline: VexRiscv): Unit = {
       execute plug new Area {
        val rs1 = U(execute.input(RS1))
        val rs2 = U(execute.input(RS2))
        val rd = UInt(32 bits)
        rd(7 downto 0) := rs1( 7 downto 0) + rs2( 7 downto 0)
        rd(16 downto 8) := rs1(16 downto 8) + rs2(16 downto 8)
        rd(23 downto 16) := rs1(23 downto 16) + rs2(23 downto 16)
        rd(31 downto 24) := rs1(31 downto 24) + rs2(31 downto 24)
        when(execute.input(IS_SIMD_ADD)) {
        execute.output(REGFILE_WRITE_DATA) := B(rd)
        }
       }
   }
}

---
CPU : Debug interface
- A CPU without a debug interface is a pity!
- The RISC-V Debug Specification is a bit heavy
- Custom requirements for a debug interface :
  - CPU controls (reset, run, halt, step)
  - CPU status (halted, breakpointed)
  - CPU god-mode (push instruction, read the result)
  - External interface (JTAG)

---
OpenOCD
- What it do :
  - Abstract the specificities of the target to GDB
  - Abstract the JTAG bridge (often a FTDI chip)
- What is required to support a new SoC :
  - A set of C functions
OpenOCD
USB
FTDI
JTAG
SoC

---
OpenOCD : Adding a new target
struct target_type vexriscv_target = {
.name = "vexriscv",
.target_create = vexriscv_target_create,
.examine = vexriscv_examine,
.halt = vexriscv_halt,
.resume = vexriscv_resume,
.step = vexriscv_step,
.add_breakpoint = vexriscv_add_breakpoint,
.remove_breakpoint = vexriscv_remove_breakpoint,
.read_memory = vexriscv_read_memory,
.write_memory = vexriscv_write_memory,
 ...
};
OpenOCD
USB
FTDI
JTAG
SoC

---
Interconnect
- Nothing complicated here
  - 1 to N (decoder)
  - N to 1 (arbiter)

---
val interconnect = PipelinedMemoryBusInterconnect()
interconnect.addSlaves(
 ram.io.bus -> SizeMapping(0x00000, 64 kB),
 peripherals.io.bus -> SizeMapping(0x70000, 64 kB),
 flashXip.io.bus -> SizeMapping(0x80000, 512 kB)
)
interconnect.addMasters(
 dBus -> List(ram.io.bus, flash.io.bus, peripherals.io.bus),
 iBus -> List(ram.io.bus, flash.io.bus)
)

---
SoC toplevel hell
- Imagine X did a SoC, then Y want to extend it for it’s own purposes, this usualy result in :
  - Y forking X SoC, and modify the toplevel (no way back, painefull pullrequest)
  - Y adding parametrization into X SoC to cover its use cases (messy SoC toplevel)
- Now Z want to extend the X SoC for it’s own purposes, ...
- Parametrization isn’t good enough !
- Solution attempt
  - Composing a SoC by having generators with dependencies and locks

---
SoC toplevel hell solution attempt
class SocX extends Generator{
   val soc = new SocBase()
   val gpioA = soc.addGpio(0xA000, 32)
}
class SocBase extends Generator{
   val cpu = new Generator { ... }
   val interconnect = new Generator { ... }
   def addGpio(address : Int, width : Int) = new Generator {
       interconnect.dependencies += this
       add task new Area {
        val ctrl = Apb3Gpio(width)
        interconnect.map(ctrl.io.bus, address, 4 KiB)
        val gpio = master(TriStateArray(width))
        gpio <> ctrl.io.gpio
       }
   }
}
class SocY extends Generator{
   val soc = new SocBase()
   val gpioA = soc.addGpio(0xA000, 12)
   val gpioB = soc.addGpio(0xA100, 16)
   val gpioC = soc.addGpio(0xA200, 20)
}

---
There is very much to do !
- New design patterns to invents
  - To squeeze more out of your ASIC/FPGA
  - To make hardware description agile
  - VHDL and Verilog are engineering bottlenecks
- Implementing hardware by using those design patterns
  - CPU, SoC, Interconnect, Peripherals, …
- Emerging HDL to support
  - SpinalHDL, Chisel, Migen, Clash, …