# Basic Types
Bool
Bits/UInt/SInt(x bits)
Vec(dataType:Data, size:Int)
object State extends SpinalEnum{ / val IDLE, S0,S1,S2 = newElement() / }

# Literals
Bool(boolean)	Val myBool = Bool(4 < 2 )
True, False	Val myBool = True
B/U/S(value:Int[,x bits])	Val myUInt = U(13, 32 bits)
B/U/S”[[size’]base]value”	Val myBits = B"8'hA3" // h,d,b,x,o
B/U/S”binaryNumber”	Val myBits = B"0110"
M”binaryNumber”	Val itMatch = myBits === M"00--10--"

# Register
val r = Reg(DataType)	val r = Reg(DataType) init(0)
val r = RegNext(signal)	val r = RegNextWhen(signal,cond)
val r = RegInit(U"010")

# Assignements
x := y	VHDL, Verilog <=
x <> y	uartCtrl.io.uart <> io.uart //Automatic connection
x \= y	VHDL :=, Verilog =

# Cast
asBits / asUInt / asSInt / asBool
x.assignFromBits(y : Bits)	Can be used to assign a Bits into something else.
x.assignFromBits(y : Bits,hi:Int,lo:Int) / x.assignFromBits(y : Bits, offset:Int, bitCount:BitCount)

# Range
myBits(7 downto 0) //8 bits	myBits(0 to 5) //6 bits
myBits(0 until 5) // 5 bits	myBits(5) //bit 5
myUInt := (default -> true)	myUInt := (myUInt.range -> true)
myUInt := (3 -> true, / default -> false)	myUInt := ((3 downto 1) -> true, / default -> false)
val myBool = myUInt === U(myUInt.range -> true)

# Units
Hz, kHz, MHz, GHz, THz	val freq:BigDecimal = 1 kHz
fs, ps, ns, us, ms, s, mn, hr	val time:BigDecimal = 2 ms
Bytes, kB, MB, GB, TB	val size:BigInt = 4MB
bits, bit	val myBits:BitCount = 3 bits

# Conditional / Mux
myBits.mux( 0 -> (io.src0 & io.src1), 1 -> (io.src0 | io.src1), default -> (io.src0) / )	when(cond1){ }.elsewhen(cond2){ }.otherwise{ }	switch(x){ is(value1){ / } is(value2){ / } default{ / } }
cond ? whenTrue | whenFalse	Select( cond1 -> value1, cond2 -> value2, default -> value3 / )
Mux(cond,whenTrue,whenFalse)

# Basetype Operators
	x + y / x – y / x * y	x < y / x > y / x <= y / x >= y	X === y / x =/= y	X >> y / x << y	X & y / x | y / x ^ y	X && y / x || y	!x	~x	##
Bool			√		√	√	√	√	√
Bits			√	√	√			√	√
Sint/UInt	√	√	√	√	√			√	√

(## for concatenation)
# Basetype Functions
Bool	.set, .clear, .rise, .fall, .setWhen(cond), .clearWhen(cond)
Bits / Sint / UInt	resize(y:Int), .resized, .range, .high, x(hi,lo), x(offset,width bits), x(index), .msb, .lsb, xorR, .orR, .andR, .clearAll, .setAll, .setAllTo(Boolean), setAllTo(Bool)

# Bundle
case class RGB(width:Int) extends Bundle{ / val red, green, blue = UInt(width bits) / def isBlack = / red === 0 & green === 0 & blue === 0 / }	val io = new Bundle{ / val a = in Bits(32 bits) / val b = in(Rgb(config)) / val c = out UInt(8 bits) / }
class Bus(val config: BusConfig) extends Bundle with IMasterSlave{ / val addr = UInt(config.addrWidth bits) / val dataWr, dataRd = Bits(config.dataWidth bits) / val cs,rw = Bool / def asMaster(): Unit = { / out(addr, dataWr, cs, rw) / in(dataRd) / } / } / val io = new Bundle{ / val masterBus = master(Bus(BusConfig)) / val slaveBus = slave(Bus(BusConfig)) / }

# Component
class AndGate(width : Int) extend Component{
  val io = new Bundle{
    val value = out Bits(width bits)
    val in1,in2 = in Bits(width bits)
  }
  io.value := io.in1 & io.in2
}
# Directions
in/out(T)	in/out Bool/Bits/UInt/SInt(x bits)
master/slave(T)	master/slave Stream/Flow(T)

# Area
val myCounter = new Area{
  val tick = Bool
  ...
}
io.output := myCounter.tick
# ClockDomain
Configuration	val myConfig = ClockDomainConfig( / clockEdge = RISING, // FALLING / resetKind = ASYNC, // SYNC, BOOT / resetActiveLevel = LOW, // HIGH / softResetActiveLevel = LOW, // HIGH / clockEnableActiveLevel = LOW // HIGH / )
Clock Domain	val myCD = ClockDomain(ioClock,ioReset, config)
Area	val coreArea = new ClockingArea(myCD){ / val myReg = Reg(UInt(32 bits)) // myCD clocked / ... / }
External Clock	val myCD = ClockDomain.external("clockName")
ClockDomain.current // Get the current clock domain

# RAM
Declaration	val myRAM = Mem(type,size:Int) / val myROM = Mem(type,initialContent : Array[Data])
Write	mem(address) := data / mem.write(address, data, [mask])
Read	myOutput := mem(x) // Asyncronous read / mem.readAsync(address,[readUnderWrite]) / mem.readSync(address,[enable],[readUnderWrite])
Read/Write	mem.readWriteSync(address,data,enable,write)

# HDL Generation
SpinalVhdl(new MyTopLevel())	SpinalVerilog(new MyTopLevel())
SpinalConfig( / mode = Verilog, // VHDL / targetDirectory="temp/myDesign", / ).generate(new myComponent())
val report = SpinalVhdl(new myTopLevel()) / report.printPruned()

# Template
import spinal.core._ // import the core
class MyTopLevel() extends Component { //Define a Component
  val io = new Bundle {
    val a,b = in Bool
    val c = out Bool
  }
  io.c := io.a & io.b
}
object MyMain {
  def main(args: Array[String]) {
    SpinalVhdl(new MyTopLevel()) //Generate a VHDL file
  }
}
# Utils
log2Up(x : BigInt)	Number of bit needed to represent x
isPow2(x : BigInt)	Return true if x is a power of two

# Function
// Function to multiply an UInt by a scala Float value. / def coef(value : UInt,by : Float ) : UInt = / (value * U((255*by).toInt,8 bits) >> 8)
def clear() : Unit = counter := 0 // Clear the counter
def sinus(size:Int, res:BitCount) = { / (0 to size).map (i => / U((Math.sin(i)+1) * Math.pow(2,res.value)/2).toInt / ) / } / // memory initialised with a sinus / val mySinus = Mem(UInt(16 bits), sinus(1024, 16 bits))

# Assertion
assert(
  assertion = cond,
  message = "My message",
  severity = ERROR //WARNING, NOTE, FAILURE
)