An alternative to standard HDL

---
Summary
- Language introduction / flow
- Simple examples
- Advanced examples
- Meta-hardware description examples

---
Language introduction
- Open source , started in december 2014
- Focus on RTL description
- Thinked to be interoperable with existing tools
  - It generate VHDL/Verilog files
  - It can integrate VHDL/Verilog IP as blackbox
Abstraction level :
  - You can design things similary to VHDL/Verilog
  - If you want to, you can use many abstraction utils and also define new ones

---
Language flow
1. Describe your RTL
2. Generate the VHDL/Verilog
3. Simulate and synthesize

---
Some points about Spinal
- There is no logic overhead in the generated code. (I swear !)
- Spinal HDL is a RTL language. But the generated VHDL/Verilog is simulatable with all standards EDA tools.
- The component hierarchy and all names are preserved during the VHDL/Verilog generation.

---
Simple examples

---
A simple component
class MyComponent extends Component {
   val io = new Bundle {
       val a = in Bool
       val result = out Bool
   }
   io.result := io.a
}
[Speaker Notes: It’s scala, but with some pretty things (in Bool in this case) New Bundle is the definition of a new datatype, a little bit like records in VHDL or struct in Verilog, but with individual element direction specification This code wire io.a to io.output]

---
Combinatorial logic
class MyComponent extends Component {
   val io = new Bundle {
       val a = in Bool
       val b = in Bool
       val c = in Bool
       val result = out Bool
   }
   io.result := (io.a & io.b) | (!io.c)
}
[Speaker Notes: Like in VHDL you can do combinatorial things. Anyway you can read the value each out signal, like a VHDL buffer.]

---
Signals
class MyComponent extends Component {
   val io = new Bundle {
       val a = in Bool
       val b = in Bool
       val c = in Bool
       val result = out Bool
   }
   val a_and_b = Bool
a_and_b := io.a & io.b
val not_c = ! io.c
io.result := a_and_b | not_c
}
[Speaker Notes: Declare what you need where you need and directly affect the value that you want (not_c signal). For example if you don’t assigne a_and_b to any value, spinalHDL tell you.]

---
Generated VHDL
entity MyComponent is
   port(
       io_a : in std_logic;
       io_b : in std_logic;
       io_c : in std_logic;
       io_result : out std_logic
   );
end MyComponent;
architecture arch of MyComponent is
   signal a_and_b : std_logic;
   signal not_c : std_logic;
begin
   io_result <= (a_and_b or not_c);
   a_and_b <= (io_a and io_b);
   not_c <= (not io_c);
end arch;
class MyComponent extends Component {
   val io = new Bundle {
       val a = in Bool
       val b = in Bool
       val c = in Bool
       val result = out Bool
   }
   val a_and_b = io.a & io.b
   val not_c = !io.c
   io.result := a_and_b | not_c
}
[Speaker Notes: As you can see you can avoid the split between the signal declaration and the signal logic.]

---
Registers
class MyComponent extends Component {
   val io = new Bundle {
       val a = in Bool
   }
   val reg1 = Reg(Bool)
val reg2 = Reg(Bool) init (False)
val reg3 = Reg(Bool)
   reg3 := ! io.a
}
[Speaker Notes: You don’t need for each register to specify his clock, it’s implicit (next clock) There is no process ! Reg1 is a simple register with no reset Reg2 is a register with a reset value at false Reg3 is the same than Reg2 with a more compact syntax Reg4 is a register that take the io.a value at each clock. You can add the init(XXX) to specify a reset value.]

---
No more Process/Always blocks
val mySignal = Bool
val myRegister = Reg(UInt(4 bits))
val myRegisterWithReset = Reg(UInt(4 bits)) init(0)
mySignal := False
when(cond) {
   mySignal := True
   myRegister := myRegister + 1
   myRegisterWithReset := myRegisterWithReset + 1
}
[Speaker Notes: In VHDL you need to split the logic between combinatoral / sequancial with reset / sequancial without reset]

---
Component instance
class SubComponent extends Component{
   val io = new Bundle {
       val input = in Bool
       val result = out Bool
   }
   ...
}
class TopLevel extends Component {
   val io = new Bundle {
       val a = in Bool
       val b = in Bool
       val result = out Bool
   }
   val sub = new SubComponent
   sub.io.input := io.a
   io.result := sub.io.result | io.b
}
[Speaker Notes: No declaration of components instances io. You directly wire it with «componentInstance.io.XXX»]

---
For, Variable, Generics
class CarryAdder(size: Int) extends Component {
   val io = new Bundle {
       val a = in UInt (size bits)
       val b = in UInt (size bits)
       val result = out UInt (size bits)
   }
   var c = False
   for (i <- 0 until size) {
       val x = io.a(i)
       val y = io.b(i)
       io.result(i) := x ^ y ^ c
       c \= (x & y) | (x & c) | (y & c);
   }
}
[Speaker Notes: This component has a construction parameter (size). It’s like generics in VHDL. The carry adder use a carry variable (c) . Variable in spinal play with scala var. If you totaly override the value of the variable, you can use the = assignement. If you do a incremental assignement, (for example a conditional (when) assignement), you must use the \= assignement operator. You can declare intermediate value (a,b) in the for. It’s as you want.]

---
Latch/Loop
val a = Bool
   val result = Bool
result := a | result //Loop detected
val result = Bool
when(cond){ //result is not assigned in all cases => Latch detected
       result := True
   }
[Speaker Notes: Spinal check if there is combinatorial loop and print a error when one is detected.]

---
ClockDomains
class MyTopLevel extends Component {
   val io = new Bundle {
       val coreClk = in Bool
       val coreReset = in Bool
   }
val coreClockDomain = ClockDomain(
       clock = io.coreClk,
       reset = io.coreReset,
       config = ClockDomainConfig(
        clockEdge = RISING,
        resetKind = ASYNC,
        resetActiveLevel = HIGH
       )
   )
   val coreArea = new ClockingArea(coreClockDomain) {
       val myCoreClockedRegister = Reg(UInt(4 bit))
       //...
   }
}

---
Function
// Input RGB color
val r,g,b = UInt(8 bits)
// Define a function to multiply a UInt by a scala Float value.
def coefMul(value : UInt,by : Float) : UInt = (value * U((255*by).toInt,8 bits) >> 8)
//Calculate the gray level
val gray = coefMul(r, 0.3f) +
        coefMul(g, 0.4f) +
        coefMul(b, 0.3f)
[Speaker Notes: In VHDL you can’t create a function that assign combinatoral and sequancial logic]

---
Function
case class Color(channelWidth: Int) extends Bundle {
   val r,g,b = UInt(channelWidth bits)
   def +(that: Color): Color = {
       val result = Color(channelWidth)
result.r := this.r + that.r
       result.g := this.g + that.g
       result.b := this.b + that.b
       return result
   }
}
[Speaker Notes: You can extend a bundle definition with all user function that you want. Here is a example where the plus operator is provided for Color Bundle(with overflow protection). You can define inner function (channelAdd) AdderAndCarry return 2 things, the sum of 2 Uint and the carry value. (scala allow return mutiple value in the same type by using Tuple)]

---
Advanced examples

---
Functional programming
val addresses = Vec(UInt(8 bits),4)
val key = UInt(8 bits)
val hits = addresses.map(address => address === key)
val hit = hits.reduce((a,b) => a || b)

---
Basic abstractions
val timeout = Timeout(1000)
when(timeout){ //implicit conversion to Bool
   timeout.clear() //Clear the flag and the internal counter
}
//Create a counter of 10 states (0 to 9)
val counter = Counter(10)
counter.clear() //When called it reset the counter. It's not a flag
counter.increment() //When called it increment the counter. It's not a flag
counter.value //current value
counter.valueNext //Next value
counter.willOverflow //Flag that indicate if the counter overflow this cycle
when(counter === 5){ …}
[Speaker Notes: Some basics abstraction are defined in the Spinal Lib.]

---
Flow, Stream
case class Flow[T <: Data](payloadType: T) extends Bundle {
   val valid = Bool
   val payload : T = cloneOf(payloadType)
}
case class Stream[T <: Data](payloadType: T) extends Bundle {
   val valid = Bool
   val ready = Bool
   val payload : T = cloneOf(payloadType)
}
val myStreamOfRGB= Stream(RGB(8,8,8))

---
Stream components
class Fifo[T <: Data](payloadType: T, depth: Int) extends Component {
   val io = new Bundle {
       val push = slave Stream (payloadType)
       val pop = master Stream (payloadType)
   }
//…
}
class Arbiter[T <: Data](payloadType: T, portCount: Int) extends Component {
   val io = new Bundle {
       val sources = Vec(slave(Stream(payloadType)), portCount)
       val sink = master(Stream(payloadType))
   }
   //...
}

---
Stream functions
case class Stream[T <: Data](payloadType: T) extends Bundle {
   // ...
   def connectFrom(that: Stream[T]) = {
       // some connections between this and that
   }
   def stage(): Stream[T] = {
       val outputStage = Stream(dataType)
       val validReg = RegInit(False)
       val payloadReg = Reg(payloadType)
       // some logic
       return outputStage
   }
   def << (that: Stream[T]) = this.connectFrom(that)
   def <-< (that: Stream[T]) = this << that.stage()
}
val myStreamA,myStreamB = Stream(UInt(8 bits))
myStreamA <-< myStreamB
[Speaker Notes: In system verilog, even if you can define interface, you can’t define function/task inside it that will generate flops and logic. This is a breaking point with systemverilog, some application of that will come in next slides]

---
Design introspection
val a = UInt(8 bits)
val b = UInt(8 bits)
val aCalcResult = complicatedLogic(a)
val aCalcResultLatency = LatencyAnalysis(a,aCalcResult)
val bDelayed = Delay(b,cycleCount = aCalcResultLatency)
val result = aCalcResult + bDelayed
[Speaker Notes: Because spinal build a netlist in the memory, you can use it to extract some information, for example latency (in cycle) between some points of you design. To do that, call LatencyAnalysis and give to it as argument some the start point, some check point and the end point of you path. It look for the shortest path and return how many cycle there is.]

---
Meta-hardware description examples

---
FSM
- They could be defined with regular syntax (Enum,Switch)
- You can also use a much more friendly syntax, fully integrated, with following features :
  - onEntry / onExit / whenIsActive / whenIsNext blocs
  - State with inner FSM
  - State with multiple inner FSM (parallel execution)
  - Delay state
  - You can extends the syntax by defining new state types

---
FSM style
val fsm = new StateMachine{
   val stateA = new State with EntryPoint
   val stateB = new State
   val stateC = new State
   val counter = Reg(UInt(8 bits)) init (0)
   io.result := False
   stateA
       .whenIsActive (goto(stateB))
   stateB
       .onEntry(counter := 0)
       .whenIsActive {
        counter := counter + 1
        when(counter === 4){
        goto(stateC)
        }
       }
       .onExit(io.result := True)
   stateC
       .whenIsActive (goto(stateA))
}
val io = new Bundle{
   val result = out Bool
}

---
Bus Slave Factory
Imagine you want to control an UART controller from a bus (for example AMBA-APB), you will have to implement a “bridge logic”.

---
Bus Slave Factory
Let’s detail the situation

---
Bus Slave Factory
BusSlaveFactory tool is able to create some “bridge logic” by using an abstract way. Let’s use it !
val bus = Apb3(addressWidth = 4, dataWidth = 32)
val uartCtrl = new UartCtrl()
val busCtrl = Apb3SlaveFactory(bus)
//Incoming “bridge logic”

---
Bus Slave Factory
Make the clockDivider readable/writable by the bus
busCtrl.driveAndRead(uartCtrl.io.config.clockDivider,address = 0)
[Speaker Notes: // Ask the busCtrl to create a readable/writable register at the address 0 // and drive uartCtrl.io.config.clockDivider with this register]

---
Bus Slave Factory
Allow the bus to read received UART frames through a FIFO
val readStream = uartCtrl.io.read.toStream.queue(rxFifoDepth)
busCtrl.readStreamNonBlocking(readStream,address = 12,validBitOffset = 31,payloadBitOffset = 0)
[Speaker Notes: // Take uartCtrl.io.read, convert it into a Stream, then connect it to the input of a FIFO // Then make the output of the FIFO readable at the address 12 by using a non blocking protocol // (bit 31 => data valid, bits 7 downto 0 => data)]

---
About FSM and Apb3SlaveFactory
Both aren’t part of Spinal core but are implemented on the top of it in the Spinal lib. Which mean these tools were created without any special interaction or special knowledge of the Spinal compiler.
They are only a mix of Scala OOP/FP with some Spinal basic syntax to generate the right hardware !

---
About Scala
Free Scala IDE (eclipse, intelij)
  - Highlight syntax error
  - Renaming flexibility
  - Intelligent auto completion
  - Code’s structure overview
  - Navigation tools
- Allow you to extend the language
- Provide many libraries

---
Spinal work perfectly on FPGA
RISCV CPU, 5 stages, 1.15 DMIPS/Mhz
  - MUL/DIV
  - Instruction/Data cache
  - Interrupts
  - JTAG debugging
- Avalon/APB UART
- Avalon VGA
- Pipelined and multi-core fractal accelerator

---
About Spinal project
Completely open source :
    - https://github.com/SpinalHDL/SpinalHDL
Online documentation :
    - https://spinalhdl.github.io/SpinalDoc/
Ready to use base project :
    - https://github.com/SpinalHDL/SpinalBaseProject
Communication channels :
    - spinalhdl@gmail.com
    - https://gitter.im/SpinalHDL/SpinalHDL
    - https://github.com/SpinalHDL/SpinalHDL/issues

---
End / Reserve slides

---
Meta-hardware description

---
Name	Type	Access	Address	Description
clockDivider	UInt	RW	0	Set the UartCtrl clock divider
frame	UartCtrlFrameConfig	RW	4	Set the dataLength, the parity and the stop bit configuration
writeCmd	Bits	W	8	Send a write command to the UartCtrl
writeBusy	Bool	R	8	Bit 0 => zero when a new writeCmd could be sent
read	Bool / Bits	R	12	Bit 7 downto 0 => fifo pop payload / Bit 31 => fifo pop valid

---
class AvalonUartCtrl(uartCtrlConfig : UartCtrlGenerics, rxFifoDepth : Int) extends Component{
   val io = new Bundle{
       val bus = slave(AvalonMM(…))
       val uart = master(Uart())
   }
   val uartCtrl = new UartCtrl(uartCtrlConfig)
   io.uart <> uartCtrl.io.uart
   val busCtrl = AvalonMMSlaveFactory(io.bus)
//Make clockDivider register
   busCtrl.driveAndRead(uartCtrl.io.config.clockDivider, address = 0)
//Make frame register
   busCtrl.driveAndRead(uartCtrl.io.config.frame, address = 4)
//Make writeCmd register
   val writeFlow = busCtrl.createAndDriveFlow(Bits(uartCtrlConfig.dataWidthMax bits), address = 8)
   writeFlow.toStream.stage() >> uartCtrl.io.write
//Make writeBusy register
   busCtrl.read(uartCtrl.io.write.valid, address = 8)
//Make read register
   busCtrl.readStreamNonBlocking(uartCtrl.io.read.toStream.queue(rxFifoDepth),
address = 12,validBitOffset = 31,payloadBitOffset = 0)
}

---
Component internal organisation
class TopLevel extends Component {
//…
   val logicArea = new Area {
       val flag = Bool
   }
val fsmArea = new Area {
        when(logicArea.flag) {
//…
}
   }
}
[Speaker Notes: There is the concept of Area, that allow you to define some sub part into a component. That help you to keep a good structure. You can use the switch statement to.]

---
UInt, Vec, When
class MyComponent extends Component {
   val io = new Bundle {
       val conds = in Vec(Bool,2)
       val result = out UInt(4 bits)
   }
   when(io.conds(0)){
       io.result := 2
       when(io.conds(1)){
        io.result := 1
       }
   } otherwise {
       io.result := 0
   }
}
[Speaker Notes: You can define a array of data elements by using Vec(numberOfElement,dataType) For hardware conditional blocks, you can use the when(cond){}.elsewhen(cond){}.otherwise {} The dot before the elsewhen is mandatory, but not for the otherwise. It’s because of scala. N.B. En each when, you can mix assignement of syncronous and asyncronous logic. You don’t have the VHDL process barrier]

---
Enum, Switch
object MyEnum extends SpinalEnum {
   val state0, state1 = newElement()
}
class MyComponent extends Component {
   val state = Reg(MyEnum) init(MyEnum.state0)
switch(state) {
       is(MyEnum.state0) {
       }
       is(MyEnum.state1) {
       }
       default{
       }
   }
}
[Speaker Notes: There is the concept of Area, that allow you to define some sub part into a component. That help you to keep a good structure. You can use the switch statement to.]

---
Memory
//Memory of 1024 Bool
val syncRam = Mem(Bool, 1024)
val asyncRam = Mem(Bool, 1024)
//Write them
syncRam(5) := True
asyncRam(5) := True
//Read them
val syncRam = mem.readSync(6)
val asyncRam = mem.readAsync(4)

---
Scala is here to help you
class SinusGenerator(resolutionWidth : Int,sampleCount : Int) extends Component {
   val io = new Bundle {
       val sin = out SInt (resolutionWidth bits)
   }
   def sinTable = (0 until sampleCount).map(sampleIndex => {
       val sinValue = Math.sin(2 * Math.PI * sampleIndex / sampleCount)
       S((sinValue * ((1 << resolutionWidth) / 2 - 1)).toInt, resolutionWidth bits)
   })
   val rom = Mem(SInt(resolutionWidth bits), initialContent = sinTable)
   val phase = CounterFreeRun(sampleCount)
   io.sin := rom.readSync(phase)
}

---
Bus Slave Factory
Allow the bus to emit UART write requests
val writeFlow = busCtrl.createAndDriveFlow(Bits(8 bits),address = 8)
writeFlow.toStream.stage >> uartCtrl.io.write
[Speaker Notes: // Ask the busCtrl to create a writable Flow[Bits] (valid/payload) at the address 8. // Then convert it into a stream, add a register register stage and connect it to the uartCtrl.io.write]

---
Bus Slave Factory
Allow the bus to get the occupancy of the write buffer
// To avoid losing writes commands between the Flow to Stream transformation just above,
// make the occupancy of the uartCtrl.io.write readable at address 8
busCtrl.read(uartCtrl.io.write.valid,address = 8)

---
Bus Slave Factory
Make the frame config readable/writable by the bus
// Do the same thing than previously but for uartCtrl.io.config.frame at the address 4
busCtrl.driveAndRead(uartCtrl.io.config.frame,address = 4)

---
FSM style A
val fsm = new StateMachine{
       io.result := False
       val counter = Reg(UInt(8 bits)) init (0)
val stateA : State = new State with EntryPoint{
        whenIsActive (goto(stateB))
       }
val stateB : State = new State{
        onEntry(counter := 0)
        whenIsActive {
        counter := counter + 1
        when(counter === 4){
        goto(stateC)
        }
        }
        onExit(io.result := True)
       }
val stateC : State = new State{
        whenIsActive (goto(stateA))
       }
   }
val io = new Bundle{
   val result = out Bool
}

---
Function, User utils (2)
class ColorSumming(sourceCount : Int, channelWidth : Int) extends Component {
   val io = new Bundle {
       val sources = in Vec(Color(channelWidth), sourceCount)
       val result = out(Color(channelWidth))
   }
   var sum = io.sources(0)
   for (i <- 1 until sourceCount) {
       sum \= sum + io.sources(i)
   }
   io.result := sum
}
[Speaker Notes: Here is a example of a block with N Color input, and a result output that is the sum of all colors by using the precedent slide plus operator.]