An alternative hardware description language

---
The Digital hardware flow

---
Issue
- The digital hardware description is done by using VHDL or Verilog
  - They are relatively low level
  - They are very verbose
  - They were not designed for this purpose

---
Solution Idea
- Using an intermediate hardware description language which
  - Generates VHDL/Verilog
  - Is dedicated for this purpose
  - Introduces new description paradigms
  - Is free and open source

---
SpinalHDL introduction
- Open source , started in december 2014
- Focus on RTL description
- Thinked to be interoperable with existing tools
  - It generates VHDL/Verilog files
  - Existing IPs can be integrated as blackboxes
- Abstraction level :
  - You can design things similarly to VHDL/Verilog
  - If you want to, you can use many abstraction utilities and also define new ones

---
Dedicated syntax
False
val mySignal = Bool
val myRegister = Reg(UInt(4 bits))
val myRegisterWithReset = Reg(UInt(4 bits)) init(0)
mySignal := False
when(cond) {
   mySignal := True
   myRegister := myRegister + 1
   myRegisterWithReset := myRegisterWithReset + 1
}
mySignal
True
cond
1
+
myRegister
4
cond
E
clk
1
+
myRegisterWithReset
4
cond
E
clk
CLR
SpinalHDL => 10 lines
VHDL => 30 lines
D
Q
D
Q
reset
[Speaker Notes: In VHDL you need to split the logic between combinatoral / sequancial with reset / sequancial without reset]

---
Interface support
  signal axiBus_aw_valid : std_logic;
  signal axiBus_aw_ready : std_logic;
  signal axiBus_aw_addr : unsigned(31 downto 0);
  signal axiBus_aw_id : unsigned(3 downto 0);
  signal axiBus_aw_region : std_logic_vector(3 downto 0);
  signal axiBus_aw_len : unsigned(7 downto 0);
  signal axiBus_aw_size : unsigned(2 downto 0);
  signal axiBus_aw_burst : std_logic_vector(1 downto 0);
  signal axiBus_aw_lock : std_logic_vector(0 downto 0);
  signal axiBus_aw_cache : std_logic_vector(3 downto 0);
  signal axiBus_aw_qos : std_logic_vector(3 downto 0);
  signal axiBus_aw_prot : std_logic_vector(2 downto 0);
  signal axiBus_w_valid : std_logic;
  signal axiBus_w_ready : std_logic;
  signal axiBus_w_data : std_logic_vector(31 downto 0);
  signal axiBus_w_strb : std_logic_vector(3 downto 0);
  signal axiBus_w_last : std_logic;
  signal axiBus_b_valid : std_logic;
  signal axiBus_b_ready : std_logic;
  signal axiBus_b_id : unsigned(3 downto 0);
  signal axiBus_b_resp : std_logic_vector(1 downto 0);
  signal axiBus_ar_valid : std_logic;
  signal axiBus_ar_ready : std_logic;
  signal axiBus_ar_addr : unsigned(31 downto 0);
  signal axiBus_ar_id : unsigned(3 downto 0);
  signal axiBus_ar_region : std_logic_vector(3 downto 0);
  signal axiBus_ar_len : unsigned(7 downto 0);
  signal axiBus_ar_size : unsigned(2 downto 0);
  signal axiBus_ar_burst : std_logic_vector(1 downto 0);
  signal axiBus_ar_lock : std_logic_vector(0 downto 0);
  signal axiBus_ar_cache : std_logic_vector(3 downto 0);
  signal axiBus_ar_qos : std_logic_vector(3 downto 0);
  signal axiBus_ar_prot : std_logic_vector(2 downto 0);
  signal axiBus_r_valid : std_logic;
  signal axiBus_r_ready : std_logic;
  signal axiBus_r_data : std_logic_vector(31 downto 0);
  signal axiBus_r_id : unsigned(3 downto 0);
  signal axiBus_r_resp : std_logic_vector(1 downto 0);
  signal axiBus_r_last : std_logic;
val config = Axi4Config(addressWidth = 32,
        dataWidth = 32,
        idWidth = 4)
val axiBus = Axi4(config)
SpinalHDL => 4 lines
VHDL => 39 lines
[Speaker Notes: In VHDL you need to split the logic between combinatoral / sequancial with reset / sequancial without reset]

---
Other features
- A proper support of
  - Design parameterization
  - Functions definition
- Many integrated checks
  - No latch
  - No combinatorial loops
  - No unwanted clock domain crossing
- And also
  - Object Oriented programming
  - Functional programming
  - Possibility to define new abstraction level
  - Meta-hardware description capabilities
  - Free IDE to make things easier

---
The technology
- SpinalHDL is an internal DSL (Domain Specific Language)
- Advantages
  - All feature the host language are inherited
  - All tools the host language are inherited
  - It makes the SpinalHDL compiler simpler
- Scala as host programming language
  - Flexible enough to have a natural syntax
- How it works
  - You compile and run your SpinalHDL hardware description
  - Each usage of SpinalHDL syntax contribute to build a netlist
  - Then this netlist go through some transformation and checks
  - Finally it is flushed into a VHDL or a Verilog file

---
Our buisness model
- No fees to use the language
  - No licence
  - No royalties
- We provide the commercial support
  - Presentation
  - Training
  - Consulting

---
Some links
Completely open source :
    - https://github.com/SpinalHDL/SpinalHDL
Online documentation :
    - https://spinalhdl.github.io/SpinalDoc/
Ready to use base project :
    - https://github.com/SpinalHDL/SpinalBaseProject
Communication channels :
    - spinalhdl@gmail.com
    - https://gitter.im/SpinalHDL/SpinalHDL
    - https://github.com/SpinalHDL/SpinalHDL/issues