An Scala internal DSL for digital designs

---
Glossary
- HDL : Hardware Description Language
- FPGA : Field-Programmable Gate Array
- SoC : System on Chip
- GPL : General Purpose Language
- DSL : Domain Specific Language

---
Summary
- DSL ? HDL ?
- SpinalHDL + examples
- Internal DSL tricks
- SoC in Scala !

---
DSL : Kinds
- External DSL
  - Dedicated syntax
  - Dedicated compiler/interpreter
  - Instances : HTML, make, …
- Internal DSL (or Embedded DSL)
  - Inherited syntax
  - Inherited compiler/interpreter
  - Instances : Embedded BASIC, Chisel, SpinalHDL, …

---
Internal DSL
- ♥
  - Reuse features of the host language
  - Reuse tools of the host language
  - Easy and fast to implement
- =(
  - Host language syntax limitations
- Example :
val orders = List[Order](
   new Order to buy(100 sharesOf "IBM")
        maxUnitPrice 300
        using premiumPricing
)

---
HDL : The Digital hardware flow

---
HDL : Example
entity TopLevel is
 port(
   a : in std_logic;
   b : in std_logic;
   c : in std_logic;
   result : out std_logic
 );
end TopLevel;
architecture arch of TopLevel is
begin
 result <= (a and b) or (not c);
end arch;

---
HDL : Misc
Instances : VHDL, Verilog
  - Low level, Verbose
  - Pain level between assembly and C
- Diferences with software programming
  - Mapped into gates and register
  - Massively parallel
  - Cycle dimension

---
SpinalHDL introduction
- Open source , started in december 2014
- Focus on hardware description
- Generates VHDL/Verilog files
- !!! Is an Scala Internal DSL !!!

---
Language flow
1. Describe your RTL
2. Generate the VHDL/Verilog
3. Simulate and synthesize

---
Keywords
- Types :
  - Bool / Bits / UInt / SInt / SpinalEnum
  - Bundle / Vec
- Hierarchy :
  - Component
  - Area
- Misc :
  - Reg / RegInit
  - in / out / master / slave

---
Simple examples

---
A simple component
class MyComponent extends Component {
   val io = new Bundle {
       val a = in Bool
       val result = out Bool
   }
   io.result := io.a
}
[Speaker Notes: It’s scala, but with some pretty things (in Bool in this case) New Bundle is the definition of a new datatype, a little bit like records in VHDL or struct in Verilog, but with individual element direction specification This code wire io.a to io.output]

---
Combinatorial logic
class MyComponent extends Component {
   val io = new Bundle {
       val a = in Bool
       val b = in Bool
       val c = in Bool
       val result = out Bool
   }
   io.result := (io.a & io.b) | (!io.c)
}
[Speaker Notes: Like in VHDL you can do combinatorial things. Anyway you can read the value each out signal, like a VHDL buffer.]

---
Signals
class MyComponent extends Component {
   val io = new Bundle {
       val a = in Bool
       val b = in Bool
       val c = in Bool
       val result = out Bool
   }
   val a_and_b = Bool
a_and_b := io.a & io.b
val not_c = ! io.c
io.result := a_and_b | not_c
}
[Speaker Notes: Declare what you need where you need and directly affect the value that you want (not_c signal). For example if you don’t assigne a_and_b to any value, spinalHDL tell you.]

---
Generated VHDL
library ieee;
use ieee.std_logic_1164.all;
use ieee.numeric_std.all;
entity MyComponent is
   port(
       io_a : in std_logic;
       io_b : in std_logic;
       io_c : in std_logic;
       io_result : out std_logic
   );
end MyComponent;
architecture arch of MyComponent is
   signal a_and_b : std_logic;
   signal not_c : std_logic;
begin
   io_result <= (a_and_b or not_c);
   a_and_b <= (io_a and io_b);
   not_c <= (not io_c);
end arch;
import spinal.core._
class MyComponent extends Component {
   val io = new Bundle {
       val a = in Bool
       val b = in Bool
       val c = in Bool
       val result = out Bool
   }
   val a_and_b = io.a & io.b
   val not_c = !io.c
   io.result := a_and_b | not_c
}
def main(args: Array[String]) {
   SpinalVhdl(new MyComponent)
}
[Speaker Notes: As you can see you can avoid the split between the signal declaration and the signal logic.]

---
How that stuff work

---
Self build graph
class Node{
 val inputs = ArrayBuffer[Node]()
}
class Bool extends Node{
 def &&(right : Bool) : Bool = ???
 def ||(right : Bool) : Bool = ???
}
class And extends Node
class Or extends Node
class Not extends Node
class MyComponent extends Component {
   val io = new Bundle {
       val a = in Bool
       val b = in Bool
       val c = in Bool
       val result = out Bool
   }
   io.result := (io.a && io.b) || (!io.c)
}

---
Self build graph
val bools = List.fill(2)(in Bool)
var boolsAnd = True
for(value <- bools){
   boolsAnd = boolsAnd && value
}
val output = out Bool()
output := boolsAnd

---
PML => Pimp My Library
implicit class StringPimper(pimped : String){
 def countUpperCases() : Int = pimped.count(_.isUpper)
}
"ChewBacca".countUpperCases() //2

---
PML : Postfixes
case class BitCount(value : Int)
implicit class IntPimper(pimped : Int){
 def bits = BitCount(pimped)
}
class UInt(width : Int)
object UInt{
 def apply(width : BitCount) = new UInt(width.value)
}
val a,b = UInt(4 bits)

---
Prefix
class BaseType extends Data{
   def asInput() : this.type = ???
}
class Bool extends BaseType
class UInt(width : Int) extends BaseType
object in{
   def Bool =
        new Bool().asInput()
   def UInt(width : BitCount) =
        new UInt(width.value).asInput()
}
val a = in Bool
val b = in UInt(4 bits)
val c = Bool().asInput()

---
Registers
class MyComponent extends Component {
   val io = new Bundle {
       val a = in Bool
   }
   val reg1 = Reg(Bool)
val reg2 = Reg(Bool) init (False)
val reg3 = Reg(Bool)
   reg3 := ! io.a
}
[Speaker Notes: You don’t need for each register to specify his clock, it’s implicit (next clock) There is no process ! Reg1 is a simple register with no reset Reg2 is a register with a reset value at false Reg3 is the same than Reg2 with a more compact syntax Reg4 is a register that take the io.a value at each clock. You can add the init(XXX) to specify a reset value.]

---
Conditional assignments
False
mySignal
val mySignal = Bool
val myRegister = Reg(UInt(4 bits))
val myRegisterWithReset = Reg(UInt(4 bits)) init(0)
mySignal := False
when(cond) {
   mySignal := True
   myRegister := myRegister + 1
   myRegisterWithReset := myRegisterWithReset + 1
}
True
cond
1
+
myRegister
4
cond
E
clk
1
+
myRegisterWithReset
4
cond
E
clk
CLR
D
Q
D
Q
reset
[Speaker Notes: In VHDL you need to split the logic between combinatoral / sequancial with reset / sequancial without reset]

---
Currying and blocks
object when {
   def apply(cond: Bool)(block: => Unit): Unit = {
       //...
       block
       //...
   }
}
val something, data, result = Bool
result := False
when(something){
   result := data
}

---
Chaining
class When(context : Bool){
   def otherwise(block : => Unit) : Unit = {
       //...
       block
       //...
   }
}
object when {
   def apply(cond: Bool)(block: => Unit): When = {
       //...
       block
       //...
       new When(cond)
   }
}
when(???){
   //...
} otherwise {
   //...
}

---
Context
object when {
   var context = List[Bool]()
   def apply(cond: Bool)(block: => Unit): Unit = {
       context = cond :: context
       block
       context = context.tail
   }
}
class Node
class Bool extends Node{
   def := (that : Bool): Unit ={
       // use when.context
   }
}

---
Component instance
class SubComponent extends Component{
   val io = new Bundle {
       val input = in Bool
       val result = out Bool
   }
   ...
}
class TopLevel extends Component {
   val io = new Bundle {
       val a = in Bool
       val b = in Bool
       val result = out Bool
   }
   val sub = new SubComponent
   sub.io.input := io.a
   io.result := sub.io.result | io.b
}
[Speaker Notes: No declaration of components instances io. You directly wire it with «componentInstance.io.XXX»]

---
For, Variable, Generics
class CarryAdder(size: Int) extends Component {
   val io = new Bundle {
       val a = in UInt (size bits)
       val b = in UInt (size bits)
       val result = out UInt (size bits)
   }
   var c = False
   for (i <- 0 until size) {
       val x = io.a(i)
       val y = io.b(i)
       io.result(i) := x ^ y ^ c
       c \= (x & y) | (x & c) | (y & c)
   }
}
[Speaker Notes: This component has a construction parameter (size). It’s like generics in VHDL. The carry adder use a carry variable (c) . Variable in spinal play with scala var. If you totaly override the value of the variable, you can use the = assignement. If you do a incremental assignement, (for example a conditional (when) assignement), you must use the \= assignement operator. You can declare intermediate value (a,b) in the for. It’s as you want.]

---
Latch/Loop
val a = Bool
   val result = Bool
result := a | result //Loop detected
val result = Bool
when(cond){ //result is not assigned in all cases => Latch detected
       result := True
   }
[Speaker Notes: Spinal check if there is combinatorial loop and print a error when one is detected.]

---
ClockDomains
class MyTopLevel extends Component {
   val io = new Bundle {
       val coreClk = in Bool
       val coreReset = in Bool
   }
val coreClockDomain = ClockDomain(
       clock = io.coreClk,
       reset = io.coreReset,
       config = ClockDomainConfig(
        clockEdge = RISING,
        resetKind = ASYNC,
        resetActiveLevel = HIGH
       )
   )
   val coreArea = new ClockingArea(coreClockDomain) {
       val myCoreClockedRegister = Reg(UInt(4 bit))
       //...
   }
}

---
Function
// Input RGB color
val r,g,b = UInt(8 bits)
// Define a function to multiply a UInt by a scala Float value.
def coefMul(value : UInt,by : Float) : UInt = (value * U((255*by).toInt,8 bits) >> 8)
//Calculate the gray level
val gray = coefMul(r, 0.3f) +
        coefMul(g, 0.4f) +
        coefMul(b, 0.3f)
[Speaker Notes: In VHDL you can’t create a function that assign combinatoral and sequancial logic]

---
Bundle and Function
case class Color(channelWidth: Int) extends Bundle {
   val r,g,b = UInt(channelWidth bits)
   def +(that: Color): Color = {
       val result = Color(channelWidth)
result.r := this.r + that.r
       result.g := this.g + that.g
       result.b := this.b + that.b
       return result
   }
}
val a,b = Color(8)
val c = a + b
val d = Color(8)
d := c
[Speaker Notes: You can extend a bundle definition with all user function that you want. Here is a example where the plus operator is provided for Color Bundle(with overflow protection). You can define inner function (channelAdd) AdderAndCarry return 2 things, the sum of 2 Uint and the carry value. (scala allow return mutiple value in the same type by using Tuple)]

---
PML : Data structure
implicit class BundlePimper[T <: Bundle](pimped : T){
   def :=(that : T) = ???
}
class RGB extends Bundle{
   val r,g,b = UInt(8 bits)
}
val a,b = new RGB
a := b //It is strongly typed and only accept RGB := RGB

---
Advanced examples

---
Functional programming
val addresses = Vec(UInt(8 bits),4)
val key = UInt(8 bits)
val hits = addresses.map(address => address === key)
val hit = hits.reduce((a,b) => a || b)

---
Basic abstractions
val timeout = Timeout(1000)
when(timeout){ //implicit conversion to Bool
   timeout.clear() //Clear the flag and the internal counter
}
//Create a counter of 10 states (0 to 9)
val counter = Counter(10)
counter.clear() //When called it reset the counter. It's not a flag
counter.increment() //When called it increment the counter. It's not a flag
counter.value //current value
counter.valueNext //Next value
counter.willOverflow //Flag that indicate if the counter overflow this cycle
when(counter === 5){ …}
[Speaker Notes: Some basics abstraction are defined in the Spinal Lib.]

---
Flow, Stream
case class Flow[T <: Data](payloadType: T) extends Bundle {
   val valid = Bool
   val payload = cloneOf(payloadType)
}
case class Stream[T <: Data](payloadType: T) extends Bundle {
   val valid = Bool
   val ready = Bool
   val payload = cloneOf(payloadType)
}
val myStreamOfRGB= Stream(RGB(8,8,8))

---
Stream components
class Fifo[T <: Data](payloadType: T, depth: Int) extends Component {
   val io = new Bundle {
       val push = slave Stream (payloadType)
       val pop = master Stream (payloadType)
   }
//…
}
class Arbiter[T <: Data](payloadType: T, portCount: Int) extends Component {
   val io = new Bundle {
       val sources = Vec(slave(Stream(payloadType)), portCount)
       val sink = master(Stream(payloadType))
   }
   //...
}

---
Stream functions
case class Stream[T <: Data](payloadType: T) extends Bundle {
   // ...
   def connectFrom(that: Stream[T]) = {
       // some connections between this and that
   }
   def stage(): Stream[T] = {
       val outputStage = Stream(payloadType)
       val validReg = RegInit(False)
       val payloadReg = Reg(payloadType)
       // some logic
       return outputStage
   }
   def << (that: Stream[T]) = this.connectFrom(that)
   def <-< (that: Stream[T]) = this << that.stage()
}
val myStreamA,myStreamB = Stream(UInt(8 bits))
myStreamA <-< myStreamB
[Speaker Notes: In system verilog, even if you can define interface, you can’t define function/task inside it that will generate flops and logic. This is a breaking point with systemverilog, some application of that will come in next slides]

---
Design introspection
val a = UInt(8 bits)
val b = UInt(8 bits)
val aCalcResult = complicatedLogic(a)
val aLatency = LatencyAnalysis(a,aCalcResult)
val bDelayed = Delay(b,cycleCount = aLatency)
val result = aCalcResult + bDelayed
[Speaker Notes: Because spinal build a netlist in the memory, you can use it to extract some information, for example latency (in cycle) between some points of you design. To do that, call LatencyAnalysis and give to it as argument some the start point, some check point and the end point of you path. It look for the shortest path and return how many cycle there is.]

---
Meta-hardware description examples

---
FSM
- They could be defined with regular syntax (Enum,Switch)
- You can also use a much more friendly syntax, fully integrated, with following features :
  - onEntry / onExit / whenIsActive / whenIsNext blocs
  - State with inner FSM
  - State with multiple inner FSM (parallel execution)
  - Delay state
  - You can extends the syntax by defining new state types

---
FSM style
val fsm = new StateMachine{
   val stateA = new State with EntryPoint
   val stateB = new State
   val stateC = new State
   val counter = Reg(UInt(8 bits)) init (0)
   io.result := False
   stateA
       .whenIsActive (goto(stateB))
   stateB
       .onEntry(counter := 0)
       .whenIsActive {
        counter := counter + 1
        when(counter === 4){
        goto(stateC)
        }
       }
       .onExit(io.result := True)
   stateC
       .whenIsActive (goto(stateA))
}
val io = new Bundle{
   val result = out Bool
}

---
Bus Slave Factory
Imagine you want to control an UART controller from a bus (for example AMBA-APB), you will have to implement a “bridge logic”.

---
Bus Slave Factory
Let’s detail the situation

---
Bus Slave Factory
BusSlaveFactory tool is able to create some “bridge logic” by using an abstract way. Let’s use it !
val bus = Apb3(addressWidth = 4, dataWidth = 32)
val uartCtrl = new UartCtrl()
val busCtrl = Apb3SlaveFactory(bus)
//Incoming “bridge logic”

---
Bus Slave Factory
Make the clockDivider readable/writable by the bus
busCtrl.driveAndRead(uartCtrl.io.config.clockDivider,address = 0)
[Speaker Notes: // Ask the busCtrl to create a readable/writable register at the address 0 // and drive uartCtrl.io.config.clockDivider with this register]

---
Bus Slave Factory
Allow the bus to read received UART frames through a FIFO
// Take uartCtrl.io.read, convert it into a Stream, then connect it to the input of a FIFO
// Then make the output of the FIFO readable at the address 12 by using a non blocking protocol
// (bit 31 => data valid, bits 7 downto 0 => data)
val readStream = uartCtrl.io.read.toStream.queue(rxFifoDepth)
busCtrl.readStreamNonBlocking(readStream,address = 12,validBitOffset = 31,payloadBitOffset = 0)

---
About FSM and Apb3SlaveFactory
Both aren’t part of Spinal core but are implemented on the top of it in the Spinal lib. Which mean these tools were created without any special interaction or special knowledge of the Spinal compiler.
They are only a mix of Scala OOP/FP with some Spinal basic syntax to generate the right hardware !

---
About Scala
Free Scala IDE (eclipse, intelij)
  - Highlight syntax error
  - Renaming flexibility
  - Intelligent auto completion
  - Code’s structure overview
  - Navigation tools
- Allow you to extend the language
- Provide many libraries

---
Spinal work perfectly on FPGA
RISCV CPU, 5 stages, 1.15 DMIPS/Mhz
  - MUL/DIV
  - Instruction/Data cache
  - Interrupts
  - JTAG debugging
- AXI/APB interconnect
- Avalon/APB UART
- Avalon/AXI VGA
- Pipelined and multi-core fractal accelerator

---
PML : String interpolation
implicit class LiteralBuilder(sc: StringContext) {
 def x(args: Any*): BigInt = BigInt(args(0).asInstanceOf[String].replace("_",""),16)
}
val literal = x"CAFE_F00D"

---
Var operator
case class MegaInt(value : Int){
   def +(that : MegaInt) = MegaInt(this.value + that.value)
}
var a = MegaInt(666)
a += MegaInt(22) //a = MegaInt(666 + 22)

---
SpinalHDL is not a joke

---
Pinsec SoC

---
Peripheral side
val timerCtrl = PinsecTimerCtrl()
val apbBridge = Axi4SharedToApb3Bridge(
   addressWidth = 20,
   dataWidth = 32,
   idWidth = 4
)
val apbDecoder = Apb3Decoder(
   master = apbBridge.io.apb,
   slaves = List(
       gpioACtrl.io.apb -> (0x00000, 4 kB),
       gpioBCtrl.io.apb -> (0x01000, 4 kB),
       uartCtrl.io.apb -> (0x10000, 4 kB),
       timerCtrl.io.apb -> (0x20000, 4 kB),
       vgaCtrl.io.apb -> (0x30000, 4 kB),
       core.io.debugBus -> (0xF0000, 4 kB)
   )
)

---
Master side
val axiCrossbar = Axi4CrossbarFactory()
axiCrossbar.addSlaves(
   ram.io.axi -> (0x00000000L, onChipRamSize),
   sdramCtrl.io.axi -> (0x40000000L, sdramLayout.capacity),
   apbBridge.io.axi -> (0xF0000000L, 1 MB)
)
axiCrossbar.addConnections(
   core.io.i -> List(ram.io.axi, sdramCtrl.io.axi),
   core.io.d -> List(ram.io.axi, sdramCtrl.io.axi, apbBridge.io.axi),
   jtagCtrl.io.axi -> List(ram.io.axi, sdramCtrl.io.axi, apbBridge.io.axi),
   vgaCtrl.io.axi -> List( sdramCtrl.io.axi)
)
axiCrossbar.build()

---
Some links
Completely open source :
    - https://github.com/SpinalHDL/SpinalHDL
Online documentation :
    - https://spinalhdl.github.io/SpinalDoc/
Ready to use base project :
    - https://github.com/SpinalHDL/SpinalBaseProject
Communication channels :
    - spinalhdl@gmail.com
    - https://gitter.im/SpinalHDL/SpinalHDL
    - https://github.com/SpinalHDL/SpinalHDL/issues