Composing an out-of-order CPU using software technics

---
NaxRiscv in short
- RV32/RV64 IMAFDCSU (Linux ready)
- Out of order / superscalar
- https://github.com/SpinalHDL/NaxRiscv
- Not implemented in VHDL/[System]Verilog
- Software abstractions and elaboration
https://twitter.com/i/status/1493996880593887235

---
Architecture
- 2 decode, 3 issue (2 ALU, 1 shared EU)
- 10 cycles miss predicted branch penalty
- 64 physical register, 64 entry ROB
- 4KB GShare, 4KB BTB (both 1 way), RAS
- Non-blocking D$
- I$ D$ each have 16 KB (4 ways)
- I$ D$ each have 192 TLB (2+4 ways)

---
Abstraction != Overhead
- RV32IMASU, 2 decode, 3 issue (Linux ready)
  - Dhrystone : 2.94 DMIPS/Mhz 1.65 IPC (-O3 -fno-common -fno-inline)
  - Coremark : 5.00 Coremark/Mhz 1.28 IPC
  - Embench-iot : 1.68 baseline 1.42 IPC (baseline = Cortex M4)
- On Artix 7 speed grade 3 :
  - 150 Mhz (360 Mhz on Kintex ultrascale+ grade 3)
  - 14.2 KLUT, 9.7 KFF, 11.5 BRAM, 4 DSP
NaxRiscv => https://spinalhdl.github.io/NaxRiscv-Rtd/main/NaxRiscv/performance/index.html

---
NaxRiscv elaboration
sbt "runMain naxriscv.Gen"
NaxRiscv => https://spinalhdl.github.io/NaxRiscv-Rtd/main/NaxRiscv/performance/index.html

---
Scala in one slides
object Main extends App{
 println("hello world")
}
object Main extends App{
 val verilog = new PrintWriter(new File("toplevel.v"))
 verilog.write("module miaou{\n")
 verilog.write(" input clk,\n")
 //...
 verilog.close()

---
Scala in one slides
object Main extends App{
 println("hello world")
object Main extends App{
 val verilog = new PrintWriter(new File("toplevel.v"))
 verilog.write("module miaou{\n")
 verilog.write(" input clk,\n")
 //...
 verilog.close()

---
Scala in one slides
object Main extends App{
 println("hello world")
object Main extends App{
 val verilog = new PrintWriter(new File("toplevel.v"))
 verilog.write("module miaou{\n")
 verilog.write(" input clk,\n")
 //...
 verilog.close()

---
SpinalHDL in two slides
import spinal.core._
object Main extends App{
 SpinalVerilog(
   new Module{
     val a,b = in UInt(8 bits)
     val result = out(a + b)
   }
 )
module unamed (
 input [7:0] a,
 input [7:0] b,
 output [7:0] result
);
 assign result = (a + b);
endmodule

---
SpinalHDL in two slides
import spinal.core._
object Main extends App{
 SpinalVerilog(
   new Module{
     val a,b = in UInt(8 bits)
     val result = out(a + b)
   }
 )
module unamed (
 input [7:0] a,
 input [7:0] b,
 output [7:0] result
);
 assign result = (a + b);
endmodule

---
SpinalHDL – Scala interaction
   new Module {
     val a,b,c = out UInt(8 bits)
     val array = ArrayBuffer[UInt]()
     array += a // By reference !
     array += b
     array += c
     for(element <- array){
       element := 0
     }
   }
module unamed (
 output [7:0] a,
 output [7:0] b,
 output [7:0] c
);
 assign a = 8'h0;
 assign b = 8'h0;
 assign c = 8'h0;
endmodule

---
SpinalHDL – Scala interaction
   new Module {
     val a,b,c = out UInt(8 bits)
     val array = ArrayBuffer[UInt]()
     array += a // By reference !
     array += b
     array += c
     for(element <- array){
       element := 0
     }
   }
module unamed (
 output [7:0] a,
 output [7:0] b,
 output [7:0] c
);
 assign a = 8'h0;
 assign b = 8'h0;
 assign c = 8'h0;
endmodule

---
SpinalHDL – Scala interaction
   new Module {
     val a,b,c = out UInt(8 bits)
     val array = ArrayBuffer[UInt]()
     array += a // By reference !
     array += b
     array += c
     for(element <- array){
       element := 0
     }
   }
module unamed (
 output [7:0] a,
 output [7:0] b,
 output [7:0] c
);
 assign a = 8'h0;
 assign b = 8'h0;
 assign c = 8'h0;
endmodule

---
SpinalHDL – API side effects
   new Module {
     val a,b,c = out UInt(8 bits)
     val array = ArrayBuffer[UInt]()
     array += a // By reference !
     array += b
     array += c
     for(element <- array){
       element := 0
     }
   }
module unamed (
 output [7:0] a,
 output [7:0] b,
 output [7:0] c
);
 assign a = 8'h0;
 assign b = 8'h0;
 assign c = 8'h0;
endmodule

---
Too many pipelines

---
Pipeline API
new Module{
 val a, b = in UInt(8 bits)
 val result = out UInt(8 bits)
 implicit val pip = new Pipeline
 val stageA = new Stage()
 val stageB = new Stage(connection = M2S())
 val stageC = new Stage(connection = M2S())
 val SUM = stageA.insert(a + b)
 result := stageC(SUM)
 pip.build()

---
Pipeline API
new Module{
 val a, b = in UInt(8 bits)
 val result = out UInt(8 bits)
 implicit val pip = new Pipeline
 val stageA = new Stage()
 val stageB = new Stage(connection = M2S())
 val stageC = new Stage(connection = M2S())
 val SUM = stageA.insert(a + b)
 result := stageC(SUM)
 pip.build()

---
Pipeline API
new Module{
 val a, b = in UInt(8 bits)
 val result = out UInt(8 bits)
 implicit val pip = new Pipeline
 val stageA = new Stage()
 val stageB = new Stage(connection = M2S())
 val stageC = new Stage(connection = M2S())
 val SUM = stageA.insert(a + b)
 result := stageC(SUM)
 pip.build()

---
Pipeline API
new Module{
 val a, b = in UInt(8 bits)
 val result = out UInt(8 bits)
 implicit val pip = new Pipeline
 val stageA = new Stage()
 val stageB = new Stage(connection = M2S())
 val stageC = new Stage(connection = M2S())
 val SUM = stageA.insert(a + b)
 result := stageC(SUM)
 pip.build()

---
Pipeline internals
class Pipeline extends Area {
  val stages = ArrayBuffer[Stage]()
  //…
  def build(): Unit = {
   for(s <- stages){
     for(... <- s.stageableToData){
     }
   }
  }
class Stage extends Area {
 val stageableToData = HashMap[Stageable, Data]()
 //…
  pip.stages += this
new Module{
 val a, b = in UInt(8 bits)
 val result = out UInt(8 bits)
 implicit val pip = new Pipeline
 val stageA = new Stage
 val stageB = new Stage(connection = M2S())
 val sum = stageA.insert(a + b)
 result := stageC(sum)
 pip.build()

---
Pipeline internals
class Pipeline extends Area {
  val stages = ArrayBuffer[Stage]()
  //…
  def build(): Unit = {
   for(s <- stages){
     for(... <- s.stageableToData){
     }
   }
  }
class Stage extends Area {
 val stageableToData = HashMap[Stageable, Data]()
 //…
  pip.stages += this
new Module{
 val a, b = in UInt(8 bits)
 val result = out UInt(8 bits)
 implicit val pip = new Pipeline
 val stageA = new Stage
 val stageB = new Stage(connection = M2S())
 val sum = stageA.insert(a + b)
 result := stageC(sum)
 pip.build()

---
Pipeline internals
class Pipeline extends Area {
  val stages = ArrayBuffer[Stage]()
  //…
  def build(): Unit = {
   for(s <- stages){
     for(... <- s.stageableToData){
     }
   }
  }
class Stage extends Area {
 val stageableToData = HashMap[Stageable, Data]()
 //…
  pip.stages += this
new Module{
 val a, b = in UInt(8 bits)
 val result = out UInt(8 bits)
 implicit val pip = new Pipeline
 val stageA = new Stage
 val stageB = new Stage(connection = M2S())
 val sum = stageA.insert(a + b)
 result := stageC(sum)
 pip.build()

---
val plugins = ArrayBuffer[Plugin]()
plugins ++= List(
   new PcPlugin(),
   new FetchCachePlugin(16 KB),
   new DecoderPlugin(),
   new DispatchPlugin(slotCount = 32),
   new CommitPlugin()
   ...
)
plugins ++= List(
   new ExecutionUnitBase("ALU0"),
   new IntAluPlugin("ALU0"),
   new ShiftPlugin("ALU0" ),
   new BranchPlugin("ALU0")
   new IntFormatPlugin("ALU0"),
   new SrcPlugin("ALU0"),
)
new NaxRiscv(plugins)
Create NaxRiscv

---
val plugins = ArrayBuffer[Plugin]()
plugins ++= List(
   new PcPlugin(),
   new FetchCachePlugin(16 KB),
   new DecoderPlugin(),
   new DispatchPlugin(slotCount = 32),
   new CommitPlugin()
   ...
)
plugins ++= List(
   new ExecutionUnitBase("ALU0"),
   new IntAluPlugin("ALU0"),
   new ShiftPlugin("ALU0" ),
   new BranchPlugin("ALU0")
   new IntFormatPlugin("ALU0"),
   new SrcPlugin("ALU0"),
)
new NaxRiscv(plugins)
Elaboration time list of Plugin

---
val plugins = ArrayBuffer[Plugin]()
plugins ++= List(
   new PcPlugin(),
   new FetchCachePlugin(16 KB),
   new DecoderPlugin(),
   new DispatchPlugin(slotCount = 32),
   new CommitPlugin()
   ...
)
plugins ++= List(
   new ExecutionUnitBase("ALU0"),
   new IntAluPlugin("ALU0"),
   new ShiftPlugin("ALU0" ),
   new BranchPlugin("ALU0")
   new IntFormatPlugin("ALU0"),
   new SrcPlugin("ALU0"),
)
new NaxRiscv(plugins)
plugins ++= List(
   new ExecutionUnitBase("ALU1"),
   new IntAluPlugin("ALU1"),
   new ShiftPlugin("ALU1" ),
   new BranchPlugin("ALU1")
   new IntFormatPlugin("ALU1"),
   new SrcPlugin("ALU1"),
)
Wanna a second execution unit ?

---
Plugin - phases
class BranchPlugin(euId : String) extends Plugin {
   val setup = create early new Area{
       // ...
   }
   val logic = create late new Area{
       // ...
   }

---
Plugin - discovery
class BranchPlugin(euId : String) extends Plugin {
 val setup = create early new Area{
    // ...
   val commit = getService[CommitService]
   val schedule = commit.newSchedulePort(canJump = true, canTrap = true)
 }
 val logic = create late new Area{
    // ...
   setup.schedule.valid := isFireing && SEL && (MISSPREDICTED || MISSALIGNED)
    setup.schedule.trap := MISSALIGNED
   setup.schedule.pcTarget := target
 }

---
Plugin – software interface
class BranchPlugin(euId : String) extends Plugin {
 val setup = create early new Area{
    // ...
   val commit = getService[CommitService]
   val schedule = commit.newSchedulePort(canJump = true, canTrap = true)
 }
 val logic = create late new Area{
    // ...
   setup.schedule.valid := isFireing && SEL && (MISSPREDICTED || MISSALIGNED)
   setup.schedule.trap := MISSALIGNED
   setup.schedule.pcTarget := target
 }

---
Plugin - implementation
class BranchPlugin(euId : String) extends Plugin {
 val setup = create early new Area{
    // ...
   val commit = getService[CommitService]
   val schedule = commit.newSchedulePort(canJump = true, canTrap = true)
 }
 val logic = create late new Area{
    // ...
   setup.schedule.valid := isFireing && SEL && (MISSPREDICTED || MISSALIGNED)
    setup.schedule.trap := MISSALIGNED
   setup.schedule.pcTarget := target
 }

---
Plugin – Composable pipeline
class BranchPlugin(euId : String) extends Plugin{
 //...
 val logic = create late new Area{
   val eu = findService[ExecutionUnitBase](_.euId == euId)
   val stage = eu.getExecute(stageId = 0)
   val target = stage(PC) + ???
    // ...
   setup.schedule.pcTarget := target
 }

---
Plugin – Composable pipeline
class BranchPlugin(euId : String) extends Plugin{
 //...
 val logic = create late new Area{
   val eu = findService[ExecutionUnitBase](_.euId == euId)
   val stage = eu.getExecute(stageId = 0)
   val target = stage(PC) + ???
    // ...
   setup.schedule.pcTarget := target
 }

---
Plugin – Adding instruction
val BEQ = SingleDecoding(
 key = M"-----------------000-----1100011",
 resources = List(
   IntRegFile -> RS1,
   IntRegFile -> RS2,
   PC_READ,
   INSTRUCTION_SIZE
 )
)
class BranchPlugin(euId : String) extends Plugin{
 val setup = create early new Area{
   val eu = findService[ExecutionUnitBase](_.euId == euId)
   eu.add(BEQ)
   // ...
 }
 //...

---
Plugin – Adding instruction
val BEQ = SingleDecoding(
 key = M"-----------------000-----1100011",
 resources = List(
   IntRegFile -> RS1,
   IntRegFile -> RS2,
   PC_READ,
   INSTRUCTION_SIZE
 )
)
class BranchPlugin(euId : String) extends Plugin{
 val setup = create early new Area{
   val eu = findService[ExecutionUnitBase](_.euId == euId)
   eu.add(BEQ)
   // ...
 }
 //...

---
Memory inferation / Netlist inspection
new Module {
 val ram = Mem.fill(256)(UInt(16 bits))
 val writeA = slave(ram.writePort())
 val writeB = slave(ram.writePort())
 val readC = slave(ram.readAsyncPort())
 val readD = slave(ram.readAsyncPort())
 this.dslBody.walkDeclarations{
   case mem : Mem[_] => {
     println(s"found $mem")
     mem.dlcForeach[Any]{
       case write : MemWrite => println(s" found one write port")
       case read : MemReadAsync => println(s" found one read port")
     }
     mem.removeStatement()
      //...
   }
   case _ =>
 }
found toplevel/ram : Mem[256*16 bits]
  found one write port
  found one write port
  found one read port
  found one read port

---
Memory inferation / Netlist inspection
new Module {
 val ram = Mem.fill(256)(UInt(16 bits))
 val writeA = slave(ram.writePort())
 val writeB = slave(ram.writePort())
 val readC = slave(ram.readAsyncPort())
 val readD = slave(ram.readAsyncPort())
 this.dslBody.walkDeclarations{
   case mem : Mem[_] => {
     println(s"found $mem")
     mem.dlcForeach[Any]{
       case write : MemWrite => println(s" found one write port")
       case read : MemReadAsync => println(s" found one read port")
     }
     mem.removeStatement()
      //...
   }
   case _ =>
 }
found toplevel/ram : Mem[256*16 bits]
  found one write port
  found one write port
  found one read port
  found one read port

---
Memory inferation / Netlist inspection
new Module {
 val ram = Mem.fill(256)(UInt(16 bits))
 val writeA = slave(ram.writePort())
 val writeB = slave(ram.writePort())
 val readC = slave(ram.readAsyncPort())
 val readD = slave(ram.readAsyncPort())
 this.dslBody.walkDeclarations{
   case mem : Mem[_] => {
     println(s"found $mem")
     mem.dlcForeach[Any]{
       case write : MemWrite => println(s" found one write port")
       case read : MemReadAsync => println(s" found one read port")
     }
     mem.removeStatement()
      //...
   }
   case _ =>
 }
found toplevel/ram : Mem[256*16 bits]
  found one write port
  found one write port
  found one read port
  found one read port

---
Memory inferation / Netlist inspection
new Module {
 val ram = Mem.fill(256)(UInt(16 bits))
 val writeA = slave(ram.writePort())
 val writeB = slave(ram.writePort())
 val readC = slave(ram.readAsyncPort())
 val readD = slave(ram.readAsyncPort())
 this.dslBody.walkDeclarations{
   case mem : Mem[_] => {
     println(s"found $mem")
     mem.dlcForeach[Any]{
       case write : MemWrite => println(s" found one write port")
       case read : MemReadAsync => println(s" found one read port")
     }
     mem.removeStatement()
      //...
   }
   case _ =>
 }
found toplevel/ram : Mem[256*16 bits]
  found one write port
  found one write port
  found one read port
  found one read port

---
Memory inferation / Netlist inspection
new Module {
 val ram = Mem.fill(256)(UInt(16 bits))
 val writeA = slave(ram.writePort())
 val writeB = slave(ram.writePort())
 val readC = slave(ram.readAsyncPort())
 val readD = slave(ram.readAsyncPort())
 this.dslBody.walkDeclarations{
   case mem : Mem[_] => {
     println(s"found $mem")
     mem.dlcForeach[Any]{
       case write : MemWrite => println(s" found one write port")
       case read : MemReadAsync => println(s" found one read port")
     }
     mem.removeStatement()
      //...
   }
   case _ =>
 }
found toplevel/ram : Mem[256*16 bits]
  found one write port
  found one write port
  found one read port
  found one read port

---
Memory inferation / Netlist inspection
new Module {
 val ram = Mem.fill(256)(UInt(16 bits))
 val writeA = slave(ram.writePort())
 val writeB = slave(ram.writePort())
 val readC = slave(ram.readAsyncPort())
 val readD = slave(ram.readAsyncPort())
 this.dslBody.walkDeclarations{
   case mem : Mem[_] => {
     println(s"found $mem")
     mem.dlcForeach[Any]{
       case write : MemWrite => println(s" found one write port")
       case read : MemReadAsync => println(s" found one read port")
     }
     mem.removeStatement()
      //...
   }
   case _ =>
 }
found toplevel/ram : Mem[256*16 bits]
  found one write port
  found one write port
  found one read port
  found one read port

---
Memory inferation / Netlist inspection
new Module {
 val ram = Mem.fill(256)(UInt(16 bits))
 val writeA = slave(ram.writePort())
 val writeB = slave(ram.writePort())
 val readC = slave(ram.readAsyncPort())
 val readD = slave(ram.readAsyncPort())
 this.dslBody.walkDeclarations{
   case mem : Mem[_] => {
     println(s"found $mem")
     mem.dlcForeach[Any]{
       case write : MemWrite => println(s" found one write port")
       case read : MemReadAsync => println(s" found one read port")
     }
     mem.removeStatement()
      //...
   }
   case _ =>
 }
found toplevel/ram : Mem[256*16 bits]
  found one write port
  found one write port
  found one read port
  found one read port

---
Questions
- SpinalHDL : https://spinalhdl.github.io/SpinalDoc-RTD/master/index.html
- NaxRiscv : https://github.com/SpinalHDL/NaxRiscv
- Roadmap :
  - Debian testing
  - Memory coherency / multicore
  - ASIC optimisation ?
- Thanks Nlnet for the funding