SaxonSoc

---
In short
- Started in parallel to VexRiscv SMP
- Based on
  - SpinalHDL “Handle” tool
  - Banana Memory Bus
- Key features
  - Memory atomics
  - Memory coherency
  - SDR/DDR2/DDR3 controller
  - Multi-core Linux
  - BMB (Memory bus)

---
ArtyA7 port

---
BMB (Banana Memory Bus)
- Goal :
  - Allow both cache-less and cache-full designs (latency / bandwidth)
  - Avoid FPGA expensive interconnects
  - No license of any sort
- Key concepts
  - cmd / rsp streams for accesses
  - cmd.context retrieved in rsp.context
  - [inv / ack / sync] stream for cache invalidation
  - [out of order]
  - Can be read write / read only / write only
  - Atomic support via load reserve / store conditional

---
BMB stream

---
cmd signals

---
rsp signals

---
inv/ack/sync

---
Handle API
- Allow :
  - Solve elaboration chunks concurrently
  - “Lazy” specification
  - Define how something should be done before having all the information you need

---
Handle API dummy example
// Create two empty Handles
val a, b = Handle[Int]
// Create a Handle which will be loaded asynchronously by the given body result
val calculator = Handle {
   a.get + b.get // .get will block until they are loaded
}
// Same as above
val printer = Handle {
   println(s"a + b = ${calculator.get}") // .get is blocking until the calculator body is done
}
// Synchronously load a and b, this will unblock a.get and b.get
a.load(3)
b.load(4)