Moving toward VexiiRiscv
Charles Papon

---
Why VexiiRiscv
- VexRiscv limits
  - Missing features : Multi-issue / RV64 / Writeback cache
  - Could have been better : Branch prediction / framework
  - The legacy : Technical debt / Ossification
- Open-source gap between single-issue in-order / out-of-order
- Expending the CPU design space you get from one design

---
VexiiRiscv design

---
VexiiRiscv feature set
- Mainly :
  - RV32/RV64, optional MAFDCBSU
  - Can run linux / buildroot / Debian
  - Optional multi-issue
  - Optional late-ALU
  - Up to 5.24 coremark/Mhz 2.50 dhystone/Mhz
  - Free / open-source
- Aswell :
  - Optional I$ D$
  - Optional BTB / RAS / Gshare branch prediction
  - RISC-V official jtag debug

---
SoC / Interconnect
- Coherent interconnect via Tilelink, optional L2
- SoC and peripherals via Litex
  - https://github.com/SpinalHDL/VexiiRiscv/blob/dev/doc/litex/debian/README.md
- USB host via OHCI
  - https://spinalhdl.github.io/SpinalDoc-RTD/master/SpinalHDL/Libraries/Com/usb_ohci.html
  - 3.3V GPIO (x2) @ 48Mhz + X*12Mhz

---
VexiiRiscv Hardware description

---
Let’s use an hardware description library
import spinal.core._
object Main extends App{
 SpinalVerilog(new Timer)
}
class Timer extends Component {
 val increment = in(Bool())
 val counter = Reg(UInt(8 bits)) init(0)
 val full = out(counter === 255)
 when(increment){
   counter := counter + 1
 }
}
module Timer (
 input wire increment,
 output wire full,
 input wire clk,
 input wire reset
);
 reg [7:0] counter;
 assign full = (counter == 8'hff);
 always @(posedge clk or posedge reset) begin
   if(reset) begin
     counter <= 8'h00;
   end else begin
     if(increment) begin
       counter <= (counter + 8'h01);
     end
   end
 end
endmodule

---
VexiiRiscv : Pipeline API

---
VexiiRiscv : Pipeline API
val aluAt = 0
val branchAt = 1
...
val alu = new pipeline.Execute(aluAt) {
 val TAKEN = insert(RS1 === RS2);
}
val branch = new pipeline.Execute(branchAt) {
 flushPort.valid := alu.TAKEN
 pcPort.valid := alu.TAKEN
 pcPort.pc := ..
}

---
No more toplevel / design space
class VexiiRiscv(...) extends Component{
 val database = ...
 val host = ...
}
val plugins = ArrayBuffer[Hostable]()
plugins += new fetch.FetchPipelinePlugin()
plugins += new fetch.PcPlugin(resetVector)
plugins += new fetch.FetchL1Plugin(...)
plugins += new prediction.BtbPlugin(...)
plugins += new prediction.GSharePlugin (...)
plugins += new prediction.HistoryPlugin(...)
...
plugins += new execute.SimdAddPlugin(...)
val cpu = VexiiRiscv(plugins)

---
SIMD add plugin

---
class SimdAddPlugin(val layer : LaneLayer) extends FiberPlugin{
 ...
 val add4 = layer.add(
    IntRegFile.TypeR(M"0000000----------000-----0001011")
  )
 add4.addRsSpec(RS1, executeAt = 0)
 add4.addRsSpec(RS2, executeAt = 0)
 add4.setCompletion(0)
//add4.mayFlushUpTo(0)
//add4.dontFlushFrom(0)
//add4.reserve(something, at=0)
 val wbp = host.find[WriteBackPlugin](p =>
    p.rf == IntRegFile && p.lane == layer.lane
  )
 val wb = wbp.createPort(at = 0)
 wbp.addMicroOp(wb, add4)
 val SEL = Payload(Bool())
 layer.lane.setDecodingDefault(SEL, False)
 add4.addDecoding(SEL -> True)
 ...
}
Scheduler
Writeback
Decoder

---
class SimdAddPlugin(val layer : LaneLayer) extends FiberPlugin{
 ...
 val process = new layer.Execute(id = 0) {
   //Get the RISC-V RS1/RS2 values from the register file
   val rs1 = layer.lane(IntRegFile, RS1).asUInt
   val rs2 = layer.lane(IntRegFile, RS2).asUInt
   //Do some computation
   val rd = UInt(32 bits)
   rd( 7 downto 0) := rs1( 7 downto 0) + rs2( 7 downto 0)
   rd(16 downto 8) := rs1(16 downto 8) + rs2(16 downto 8)
   rd(23 downto 16) := rs1(23 downto 16) + rs2(23 downto 16)
   rd(31 downto 24) := rs1(31 downto 24) + rs2(31 downto 24)
   //Provide the computation value for the writeback
   wb.valid := isValid && SEL
   wb.payload := rd.asBits
 }
  ...
}

---
Looking for contributions
- Already a few
  - RVB (Andreas Wallner)
  - Compact divider (Thomas Kramer)
- Looking for help
  - Features additions
  - Alternative implementations
  - Performance improvements
  - Testing
  - ASIC port
  - …
- https://github.com/SpinalHDL/VexiiRiscv

---
Tooling
- SpinalHDL / Scala : Hardware generation
- Litex : SoC generation and deployment
- Spike / RVLS : RISC-V golden model and lock-step checker
- Verilator : Fast simulation
- Konata : CPU pipeline visualisation