SpinalHDL
Paradigm introduction
WOSH, June 2019

---
Introduction
- What is SpinalHDL ?
  - It is a tool to design digital hardware like Chisel and FHDL
- Why those language exists ?
  - Because some people aren’t satisfied of VHDL / Verilog / SystemVerilog

---
SpinalHDL is embedded into a general purpose language
import spinal.core._
class MyToplevel extends Component{
 val a,b = in UInt(8 bits)
 val result = out UInt(8 bits)
 result := a + b
}
object Main extends App{
 SpinalVerilog(new MyToplevel)

---
You can describe the same kind of things than VHDL/Verilog/...
class MyToplevel extends Component {
 //...
 val counter = Reg(UInt(8 bits))
 val full = counter === 255
 when(!full) {
   counter := counter + 1
 }
 //...

---
Synergy between SpinalHDL and Scala
val cond = Bool()
val a, b, c = Reg(UInt(8 bits))
val regs = ArrayBuffer[UInt]()
regs += a
regs += b
regs += c
when(cond) {
 for(reg <- regs) {
   reg := reg + 1
 }
val cond = Bool()
val a, b, c = Reg(UInt(8 bits))
when(cond) {
 a := a + 1
 b := b + 1
 c := c + 1

---
Register bank : The regular way
val bus = Apb3(addressWidth = 16, dataWidth = 32)
val regA, regB = Reg(Bits(32 bits))
val doWrite = bus.PSEL(0) && bus.PENABLE && bus.PWRITE
switch(bus.PADDR){
 is(0x00){
   when(doWrite){ regA := bus.PWDATA }
   bus.PRDATA := regA
 }
 is(0x04){
   when(doWrite){ regB := bus.PWDATA }
   bus.PRDATA := regB
 }

---
Register bank : Using a specification
val bus = Apb3(addressWidth = 16, dataWidth = 32)
val regA, regB = Reg(Bits(32 bits))
case class Mapping(address : Int, data : Bits)
val spec = ArrayBuffer[Mapping]()
spec += Mapping(0x00, regA)
spec += Mapping(0x04, regB)
val doWrite = bus.PSEL(0) && bus.PENABLE && bus.PWRITE
switch(bus.PADDR){
 for(mapping <- spec){
   is(mapping.address){
     when(doWrite){ mapping.data := bus.PWDATA }
     bus.PRDATA := mapping.data
   }
 }

---
Register bank : Defining a tool
case class Apb3Mapper(bus : Apb3) {
 val spec = ArrayBuffer[Mapping]()
 def flush() {
   val doWrite = bus.PSEL(0) && bus.PENABLE && bus.PWRITE
   switch(bus.PADDR) {
     for (mapping <- spec) {
       is(mapping.address) {
        when(doWrite) {
        mapping.data := bus.PWDATA
        }
        bus.PRDATA := mapping.data
       }
     }
   }
 }

---
Register bank : Tool usage
val bus = Apb3(addressWidth = 16, dataWidth = 32)
val regA, regB = Reg(Bits(32 bits))
val mapper = Apb3Mapper(bus)
mapper.mapping += Mapping(0x00, regA)
mapper.mapping += Mapping(0x04, regB)
mapper.flush()

---
Register bank : Hiding the tool internals
case class Apb3Mapper(bus: Apb3) {
 ...
 def readWrite(address: Int, data: Bits) = {
    spec += Mapping(address, data)
  }.
val bus = Apb3(addressWidth = 16, dataWidth = 32)
val regA, regB = Reg(Bits(32 bits))
val mapper = Apb3Mapper(bus)
mapper.readWrite(0x00, regA)
mapper.readWrite(0x04, regB)
mapper.flush()

---
Register bank : More API
case class Apb3Mapper(bus : Apb3) {
 // ...
 def createReadWrite(address : Int) : Bits = {
   val reg = Reg(Bits(32 bits))
   spec += Mapping(address, reg)
   return reg
 }
 // ...
val bus = Apb3(addressWidth = 16, dataWidth = 32)
val mapper = Apb3Mapper(bus)
val regA = mapper.createReadWrite(0x00)
val regB = mapper.createReadWrite(0x04)
mapper.flush()

---
SpinalHDL is embedded into a general purpose language
General purpose programming language + HDAPI
Hardware netlist
import spinal.core._
Execution
Netlist flush
VHDL/Verilog
val reg2 = Reg(UInt(8 bits)) init(0)
when(cond){
 reg2 := 50
val reg1 = Reg(UInt(8 bits))
val cond = reg1 === 42

---
Introduction
    val cond = in Bool()
    val a, b, c = Reg(UInt(8 bits))
    when(cond) {
      a := a + 1
      b := b + 1
      c := c + 1
    }

---
The SpinalHDL hardware API
- Hardware types (Bool, Bits, UInt, SInt, Bundle, Vec, …)
- Hardware conditional statements (when, switch)
- Hardware operators (:=, + - * / %, && || ^ ~, ...)
- And few others hardware constructs (Component, in, out, Area, ClockDomain, …)

---
Just some points before continuing
- About SpinalHDL
  - There is no logic overhead in the RTL
  - Will not generate broken VHDL/Verilog
    - check latches, combinatorial loop, signal width mismatch, …
  - SpinalHDL isn't a language, it's a HDAPI in Scala
- But this talk isn't realy about SpinalHDL
  - It will not introduce much of the SpinalHDL syntax
  - It will focus on giving you keys example to “feel” some of the semantic of HDAPI (SpinalHDL, Chisel, FHDL, …)

---
Semantic example
All the SpinalHDL API call which fill the netlist are in red
Everything else is Scala
//** Standard implementation**
val condA, condB = Bool()
val result = UInt(8 bits)
result := U(0) //Can also be := 0
when(condA) {
   result := U(42)
when(condB) {
   result := U(255)
Scala

---
Semantic example
All the SpinalHDL API call which fill the netlist are in red
Everything else is Scala
//** Implementation via function/reference**
val condA, condB = Bool()
val result = UInt(8 bits)
result := U(0)
//Function call will be inlined in the netlist
whenAssign(condA, result, U(42))
whenAssign(condB, result, U(255))
def whenAssign(condition: Bool, target: UInt, value: UInt) = {
   when(condition) {
       target := value
   }
//** Standard implementation**
val condA, condB = Bool()
val result = UInt(8 bits)
result := U(0) //Can also be := 0
when(condA) {
   result := U(42)
when(condB) {
   result := U(255)
Scala

---
Semantic example
//** Generation via a software model **
val condA, condB = Bool()
val result = UInt(8 bits)
result := U(0)
val spec = ArrayBuffer[SpecElement]() //Scala dynamic array of SpecElement
class SpecElement(val cond: Bool, val target: UInt, val source: UInt)
spec += new SpecElement(condA, result, U(42))
spec += new SpecElement(condB, result, U(255))
//Loop iterations will be inlined in the netlist
for(e <- spec){
   when(e.cond){
       e.target := e.source
   }
Scala

---
Simple peripheral design
- Let's imagine a simple peripheral which do XOR operations
  - We want to access it from a memory bus
  - So we need to create a bridge between the memoryBus and the peripheral signals (a, b, result)
- Let's implement it.

---
Peripheral implementation (with APB3)
val a, b = Reg(Bits(32 bits))
val result = a ^ b
//Create a new APB3 bus
val memoryBus = Apb3(addressWidth = 8, dataWidth = 32)
//Create the factory which creates the bridging logic between the bus and some hardware
val memoryMapper = new Apb3MemoryMapper(memoryBus)
//Drive 'a' and 'b' from the memoryBus
memoryMapper.write(target=a, address = 0x00)
memoryMapper.write(target=b, address = 0x04)
//Make 'result' readable by memoryBus
memoryMapper.read(source=result, address = 0x08)
memoryMapper.build()

---
Memory mapping datamodel
class WriteAccess(val target : Bits)
class ReadAccess(val source : Bits)
class Apb3MemoryMapper(bus : Apb3) {
 val spec = Map[Int, ArrayBuffer[Any]]()
 def write(target : Bits, address : Int) = spec(address) += new WriteAccess(target)
 def read(source : Bits, address : Int) = spec(address) += new ReadAccess(source)
 def build() = { … } // Implementation on the next slide

---
Memory mapping APB3 implementation
class Apb3MemoryMapper(bus : Apb3) {
   override def build() = {
        ...
   }

---
Memory mapping APB3 implementation
class Apb3MemoryMapper(bus : Apb3) {
   override def build() = {
        ...
       val doWrite = bus.PSEL(0) && bus.PENABLE && bus.PREADY && bus.PWRITE
   }

---
Memory mapping APB3 implementation
class Apb3MemoryMapper(bus : Apb3) {
   override def build() = {
        ...
       val doWrite = bus.PSEL(0) && bus.PENABLE && bus.PREADY && bus.PWRITE
       switch(bus.PADDR) { // Hardware switch statement
       }
   }

---
Memory mapping APB3 implementation
class Apb3MemoryMapper(bus : Apb3) {
   override def build() = {
        ...
       val doWrite = bus.PSEL(0) && bus.PENABLE && bus.PREADY && bus.PWRITE
       switch(bus.PADDR) {
        for ((address, jobs) <- spec) { // Software loop
        }
       }
   }

---
Memory mapping APB3 implementation
class Apb3MemoryMapper(bus : Apb3) {
   override def build() = {
        ...
       val doWrite = bus.PSEL(0) && bus.PENABLE && bus.PREADY && bus.PWRITE
       switch(bus.PADDR) {
        for ((address, jobs) <- spec) {
        is(address) { // Hardware is statement
        }
        }
       }
   }

---
Memory mapping APB3 implementation
class Apb3MemoryMapper(bus : Apb3) {
   override def build() = {
        ...
       val doWrite = bus.PSEL(0) && bus.PENABLE && bus.PREADY && bus.PWRITE
       switch(bus.PADDR) {
        for ((address, jobs) <- spec) {
        is(address) {
        for(job <- jobs) { // Software loop statement
        }
        }
        }
       }
   }

---
Memory mapping APB3 implementation
class Apb3MemoryMapper(bus : Apb3) {
   override def build() = {
        ...
       val doWrite = bus.PSEL(0) && bus.PENABLE && bus.PREADY && bus.PWRITE
       switch(bus.PADDR) {
        for ((address, jobs) <- spec) {
        is(address) {
        for(job <- jobs) job match { // Software switch statement
        case w : WriteAccess => ...
        case r : ReadAccess => ...
        }
        }
        }
       }
   }

---
Memory mapping APB3 implementation
class Apb3MemoryMapper(bus : Apb3) {
   override def build() = {
        ...
       val doWrite = bus.PSEL(0) && bus.PENABLE && bus.PREADY && bus.PWRITE
       switch(bus.PADDR) {
        for ((address, jobs) <- spec) {
        is(address) {
        for(job <- jobs) job match {
        case w : WriteAccess => when(doWrite) { w.target := bus.PWDATA }
        case r : ReadAccess => bus.PRDATA := r.source
        }
        }
        }
       }
   }

---
And the drive primitive ?
- Build on the top of the write primitive
- You can do the same for many other primitives, ex : driveAndRead
class Apb3MemoryMapper(bus : Apb3) {
   ...
    def write(target : Bits, address : Int) = ...
   def read(source : Bits, address : Int) = ...
   def drive(target : Bits, address : Int) = {
       val driver = Reg(Bits(widthOf(target) bits))
       target := driver
       write(driver, address)
   }

---
Let's do proper software enginnering
abstract class MemoryMapper{
 val spec = HashMap[Int, ArrayBuffer[Any]]()
 def write(target : Bits, address : Int) =...
 def read(source : Bits, address : Int) = ...
 def build() = ??? // Unimplemented
We are now bus agnostic !
class Apb3MemoryMapper(bus : Apb3) extends MemoryMapper{
   override def build() = {
        ...
   }
class Something extends Bundle{
   val a, b = UInt(32 bits)
   def readFrom(factory : MemoryMapper) = {
       factory.read(a, address = 0x00)
       factory.read(b, address = 0x04)
   }

---
VexRiscv : A CPU implemented with SpinalHDL
- RV32I[M][C], 5 stages
- Optional I$ D$
- Optional JTAG with openocd port
- On Artix7 FPGA :
  - 500 to 2000 LUT
  - 200 to 340 Mhz
  - 0.51 to 1.44 DMIPS/Mhz (Drystone 2.1, -O3 -fno-inline)
- But the implementation isn't usual
VexRiscv
VexRiscv / Plugins
Pipeline framework
Scala / SpinalHDL

---
Modular CPU framework
val config = VexRiscvConfig()
config.plugins ++= List(
  new IBusSimplePlugin(resetVector = 0x80000000l),
  new DBusSimplePlugin,
  new CsrPlugin(CsrPluginConfig.smallest),
  new DecoderSimplePlugin,
  new RegFilePlugin(regFileReadyKind = plugin.SYNC),
  new SrcPlugin,
  new IntAluPlugin,
  new BranchPlugin(earlyBranch = false),
  new MulDivIterativePlugin(
     mulUnrollFactor = 4,
     divUnrollFactor = 1
  ),
  new FullBarrelShifterPlugin,
  new HazardSimplePlugin,
  new YamlPlugin("cpu0.yaml")
)
new VexRiscv(config)

---
CPU framework - Connections
insert map
pipeline table
//Global definition of the Programm Counter concept
object PC extends Stageable(UInt(32 bits))
//Somewere in the plugin which manage the program counter
decode.insert(PC) := X
//Somewere in the MachineCsr plugin
Y := writeBack.input(PC)
Key
Value
Index
Stage
PC
X
0
decode
...
...
1
execute
2
memory
input map
3
writeback
Key
Value
PC
Y
...
...

---
CPU framework - Connections
//Somewhere in the Branch plugin
val jumpInterface = pcPlugin.createJumpInterface(stage = execute)
//Later in the branch plugin
jumpInterface.valid := wannaJump
jumpInterface.payload := execute.input(PC) + execute.input(INSTRUCTION)(31 downto 20)

---
Plugin example : 4x8bits add (SIMD)
class SimdAddPlugin extends Plugin[VexRiscv]{
   override def setup(pipeline: VexRiscv): Unit = {
       ...
   }
   override def build(pipeline: VexRiscv): Unit = {
       ..
   }

---
class SimdAddPlugin extends Plugin[VexRiscv]{
   object IS_SIMD_ADD extends Stageable(Bool)
   override def setup(pipeline: VexRiscv): Unit = {
       val decoderService = pipeline.service(classOf[DecoderService])
       decoderService.addDefault(IS_SIMD_ADD, False)
       decoderService.add(
        key = M"0000011----------000-----0110011",
        List(
        IS_SIMD_ADD -> True,
        REGFILE_WRITE_VALID -> True,
        BYPASSABLE_EXECUTE_STAGE -> True,
        BYPASSABLE_MEMORY_STAGE -> True,
        RS1_USE -> True,
        RS2_USE -> True
        )
       )
   }
   override def build(pipeline: VexRiscv): Unit = { .. }

---
class SimdAddPlugin extends Plugin[VexRiscv]{
   object IS_SIMD_ADD extends Stageable(Bool)
   override def setup(pipeline: VexRiscv): Unit = { .. }
   override def build(pipeline: VexRiscv): Unit = {
       execute plug new Area {
        val rs1 = U(execute.input(RS1))
        val rs2 = U(execute.input(RS2))
        val rd = UInt(32 bits)
        rd(7 downto 0) := rs1(7 downto 0) + rs2(7 downto 0)
        rd(16 downto 8) := rs1(16 downto 8) + rs2(16 downto 8)
        rd(23 downto 16) := rs1(23 downto 16) + rs2(23 downto 16)
        rd(31 downto 24) := rs1(31 downto 24) + rs2(31 downto 24)
        when(execute.input(IS_SIMD_ADD)) {
        execute.output(REGFILE_WRITE_DATA) := B(rd)
        }
       }
   }

---
The end, tips to think about all of this
- When you execute the scala code, each SpinalHDL API call will add information in the SpinalHDL netlist
- All the elaborated features come from Scala (host general purpose language)
- None of the previous slide require SpinalHDL modifications, they are all implemented on the top of SpinalHDL/Scala
- Don't take the previous slide as a “You should use this framework” but as demonstration / proof of concept

---
Some links
- SpinalHDL library sources :
  - https://github.com/SpinalHDL/SpinalHDL
- Online documentation :
  - https://spinalhdl.github.io/SpinalDoc/
- Ready to use base project :
  - https://github.com/SpinalHDL/SpinalTemplateSbt
- Communication channels :
  - spinalhdl@gmail.com
  - https://gitter.im/SpinalHDL/SpinalHDL